## Slide 1
QOSPF: Quality of Service Extensions to OSFP or Quality of Service Path First Routing
Eric S. Crawley
Bay Networks, Inc.
esc@baynetworks.com

## Slide 2
The Challenge
Protocol Overview
Scaling Problems
The Details
The Remaining Problems
Overview

## Slide 3
The Challenge
A customer asked us to combine MOSPF and RSVP to provide Quality of Service routing in a WAN environment
The WAN was mostly T-1 links but sufficiently redundant that there were multiple paths between multicast sources and destinations
The application closely matched the “Cable TV” type of environment
  Single sender
  Multiple receivers coming and going
  Fast receiver JOIN times needed (< 2 sec)

## Slide 4
Example Topology
T-1
Lines
Sender
Receiver
If Resources are
not available on
usual path
A path is calculated that
has the resources to
support the flow

## Slide 5
Basic Protocol Steps
Network resources are advertised to the area
Trigger event causes calculation of QoS route (demand driven)
  RSVP messages containing resource requirements
QoS route is computed as needed by routers on path
Notification of actual reservation of resources to assure that path computation was correct and “store state”
QoS route is removed when trigger events disappear (RSVP PATH state times out)

## Slide 6
Protocol Overview: Resource Advertisements
New OSPF LSAs for advertising router link resources
  Controlled Load Model used
    Advertise Largest chunk of reservable BW
    Advertise Largest buffer/burst reservable
    For each link
Other service models/parameters can/should be added
Provides information for QoS routing calculation

## Slide 7
Protocol Overview: Route Computation
QoS Dijkstra calculation triggered by receipt of new RSVP PATH message
  Other triggers such as different signaling protocols and flow thresholds can be used
  Multicast uses Group Membership LSAs for member list
  QoS route computed for Source->Destination pair
  This means all traffic for Source->Destination pair is routed on same path
Only Links with adequate resources are used for Dijkstra
  Recovery to best-effort path possible

## Slide 8
Protocol Overview: Confirmation/Recalculation
Success on RESV triggers Opaque LSA indicating reservation on link for Source->Destination pair
Recomputation could occur on RESV if resources different from PATH
Routes may be pinned (e.g. not changed by new links or more resources becoming available)
New resource LSAs (reserved and available) and topology changes cause recalculation favoring links currently reserved for flow

## Slide 9
Example
Sender
Rcvr 1
Rcvr 2
Rcvr 3
1. RCVRs 1,2,&3 have joined group G
2. RSVP PATH Message sent from sender to G
3. R1 Computes QoS Path to RCVRs 1,2,&3
- Link L1 does not have adequate resources for flow
based on RSVP TSpec
- Tree is computed using L2, L3, and L4
4. Process is repeated for R2, R3, and R4 as PATH message
travels down tree
5. Rcvrs send RESV message back toward sender,
reserving resources
6. Routers send Resource reserved advertisements
indicating the resources used for the Source, Group pair
7. If significant resources are used, routers send new
Resource Available advertisements
R1
R2
R3
R4
L1
L2
L3
L4

## Slide 10
Why are Resource Reserved Advertisements Needed?
Need to save tree state somehow
  For adding new members and knowing what branches are currently in use
  So new resource available advertisements don’t affect paths currently in use (AKA “Stepping on your own Shadow”)

## Slide 11
Scaling Problems
Resource Available LSAs can be sent out too frequently
  Solution: Use watermarks and/or resource reserved > resource available comparisons
Resource Reserved Advertisements are flooded for every link on source->destination path generated on receipt of RESV
  Solution: Explicit Routing

## Slide 12
Explicit Routing (EROSPF)
A router, usually the source router, computes the QoS route path from source->destination
The route computation is passed down the tree using opaque LSAs (Explicit Route Advertisements, ERAs)
ERAs encode the route in such a way that no recomputation is necessary for each router along the path
Routes can be broken up into multiple ERAs to avoid MTU limits
Resource Reserved Advertisements need only be sent back to the computing/source router
Flushing ERAs are used to remove routes

## Slide 13
Explicit Routing Example
Sender
Rcvr 1
Rcvr 2
Rcvr 3
1. RCVRs 1,2,&3 have joined group G
2. RSVP PATH Message sent from sender to G
3. R1 Computes QoS Path to RCVRs 1,2,&3
- Link L1 does not have adequate resources for flow
based on RSVP TSpec
- Tree is computed using L2, L3, and L4
4. R1 sends ERA to R3 with subtree of R2 and R4
5. R3 installs ERA state and sends ERAs to R2 and R4
6. Process is repeated on R2 and R4 installing state
7. Rcvrs send RESV message back toward sender,
reserving resources
8. Routers send Resource reserved advertisements only to
R1 indicating the resources used for the Source, Group
pair
R1
R2
R3
R4
L1
L2
L3
L4

## Slide 14
OSPF/MOSPF Extensions
Resource Available LSA
Resource Reservation Advertisement
Explicit Route Advertisements
Border Router Advertisements
Route Computation Changes

## Slide 15
Resource Available LSA (RES-LSA)
Flooded through Area
Token Bucket parameters are single precision floating point (IntServ std)
Link Delay is used in place of TOS 0 metric for QoS route calculation
Could be expanded for other service models

## Slide 16
Resource Reservation Advertisement (RRA)
Flooded “Area Local” without ER
Flooded “No Flooding” and “Link Local” with ER
Source and Destination are the IP source and destination addresses
Pin Flag indicates whether route pinning has been requested

## Slide 17
Explicit Route Advertisement (ERA)
“No Flooding” scope
ERA header indicates source-> destination pair
ERA body encodes path
Adjust Offset is used to avoid recomputing offsets for subsequent ERAs
Child offset indicates next child in for interface
LSA Age = MAXAGE indicates flushing LSA

## Slide 18
Border Router Advertisement (DABRA)
Indicates to “downstream” areas how to root a tree (which area border router to use) for source->destination
Flooded to all downstream areas from borders that receive flow without ER
Sent only to border routers on path with ER

## Slide 19
Route Computation Changes
Topology Change - all routes recomputed (conventional or QoS)
  Must use RRAs to determine resources used by current path and pinned routes
New MOSPF Group Membership LSAs
New RES-LSAs - all QoS routes recomputed
New RRAs - all QoS routes related to the RRAs recomputed
New DABRAs- all QoS routes related to the DABRAs recomputed

## Slide 20
Multicast Issues
Adding members/branches can be tricky so you don’t “avoid your own shadow”
  Must know where current distribution tree passes
Border router issues are interesting
  Enough information to prevent loops
  Not too much to keep summarization
Solutions may be very different for shared tree protocols
Interdomain solutions will be very interesting...

## Slide 21
Possible RSVP Additions
Route pinning flag so receivers can request a “pinned” route
  Possible length of time to pin a route?
Indication that a RESV differs from a PATH to help determine if recalculation is needed

## Slide 22
Remaining Problems
Unicast can possible suffer from route loops if packets “fall off” the QoS computed path
  May need to tag or mark packets on QoS paths to note different treatment (TOS bits or Flow ID?)
  If packets “fall off” QoS path mark is removed
Need to think through other RSVP reservation styles (SE & WF)
Need more experience, simulation, and real use