## Slide 1
Agenda
Introduction and Agenda Bashing
Purpose
What is the problem?
Issues for QoS Routing: Bala Rajagopalan
More QoS Routing Issues: Ross, Eric, Joel
QOSPF: Eric
Other Work
Next Steps

## Slide 2
Purpose
Discuss some of the issues related to Quality of Service (QoS) Routing
Note some of the current work related to QoS Routing
Determine if this work belongs in existing working groups
Determine if a new WG should be created

## Slide 3
What’s the Problem?
We could have QoS Signaling (RSVP, etc.) without QoS Routing but...
If the topology has multiple paths between a source and destination and there are insufficient resources available on the “shortest” path, it would be nice to use resources that are available on other paths

## Slide 4
Example
Sender
Receiver
Insufficient resources are
available on “shortest” path
QoS Routing would
allow the flow to travel
over another path that
can support the flow

## Slide 5
More QoS Routing Issues
Route Pinning
“Avoiding your own shadow”
Route management to avoid loops
Multiple routes for multiple flows between the same source->destination pairs
Heterogeneous QoS

## Slide 6
Route Pinning
Route / Resource stability
Avoid instabilities based on “avoiding own shadow” issue
Work with Explicit Routes
Coordination with ATM (keep IP flow lined up with ATM SVC).

## Slide 7
Route Stability
Changes in routing can cause disruption to real-time applications
If new routes become available, some applications may not want to relinquish the route that they already have
Applications requesting resources should have the ability to ask for a path that does not change except on link failure
It might make sense to consider a timer on route pinning to avoid convoluted routing that is possible by pinning a “transient” route

## Slide 8
“Avoiding Your own Shadow”
If a path is created that uses some amount of network resource, and advertisements announce resulting reduction in available resource, existing flows (which already have their resources reserved) shouldn’t avoid their current links
  Think of what would happen if you try to energetically avoid your own shadow (drugs available for people, computers are more persistent)

## Slide 9
Explicit (aka Source) Routing
Retry after failure, using different route which avoids the point of failure
Add new branch to an existing tree (meet sooner rather than later)
Extensibility (if some routers support new service, but not all)
Datagram re-route issues -- pinned route needs explicit routing
Efficiency: ER needs to use route pining

## Slide 10
Route Management to Avoid Loops
If a QoS path does not match a best effort path and part of the QoS path fails such that packets from the QoS path flow to the best effort path, It is possible for a route loop to be created
It may make sense to “tag” packets on the QoS path to note their “special treatment” and remove the tag should a packet be forwarded off the QoS path
IPv6 Flow ID and IPv4 TOS bits are possible tagging mechanisms

## Slide 11
Multiple Routes
Routing usually deals with destination routes
Multicast routing can use source->destination pair
QoS signaling can use Source, Destination, Protocol, and Port
Should routing use layer 4 information to distinguish flows?
Forwarding tables can get very large!
IPv6 Flow ID can also be used

## Slide 12
Heterogeneous QoS
RSVP allows different receivers to specify different QoS values for the same flow
QoS routing must be able to calculate or handle the “variegated” trees possible

## Slide 13
Other QoS Routing Work
I-PNNI
  ATM Forum
  Layer 3 routing that uses ATM PNNI routing information
Nimrod

## Slide 14
Next Steps
Are there WGs to address these issues?
Is there sufficient interest for a QoSR WG?
Need:
  Charter
  Mailing List
  WG Chairs
  Approval of AD and IESG