## Slide 1: ON AN IMPROVED WAY OF RESOLVING TWO VERY STABLE AND ACCURATE FREQUENCY SIGNALS AND THE BENEFITS CONFERRED AS A RESULT
Richard Percival
Quartzlock (UK) Ltd

## Slide 2: A7 Frequency and Phase Comparator
Introduction and modes of operation
Hardware description
Modes of operation
Performance specifications
Applications
Other points/conclusions

## Slide 3: Introduction
What is the A7
What are the uses for the A7
What is special about this instrument

## Slide 4: Definitions
Frequency
Gate Time
Frequency Accuracy
Frequency Stability
Reciprocal counting
Time Interval

## Slide 5: Hardware Description
Overview of A7
Frequency Difference Multiplier
Distribution Amplifier
Internal Rubidium Oscillator
GT200 Time Interval Counter

## Slide 6: Overview of A7
Consists of a frequency difference multiplier (Integral) surrounded by a distribution amplifier, rubidium oscillator, supporting electronics and Time Interval counter
19” 2U rack mountable unit with user operable front panel

## Slide 7: Frequency Difference Multiplier
Extremely high quality module multiplies very small frequency differences so they may resolved by standard 100ps TIC
Operates on both 5 and 10 MHz inputs
Two modes of operation
  Frequency
  Phase/Time

## Slide 8: Distribution Amplifier
Linear frequency distribution 1….100 MHz
1 input and 4 outputs
Hydrogen maser compatible performance
Separate circuitry from A7 main unit
Adjustable gain, low phase noise, high isolation & low channel-channel crosstalk

## Slide 9: Internal Rubidium Oscillator
Enables suitable reference signal for medium to high application
Small size, low weight, high accuracy & high stability
Turns A7 into complete frequency generation, measurement and distribution system. Complete metrology solution !

## Slide 10: GT200 Time Interval Counter
Universal Time Interval counter using reciprocal time counting
PC interfacing and associated software provides virtual front panel
May be replaced by user with any suitable time interval counter
Enables automatic data acquistion

## Slide 11: Modes of Operation
Introduction
Frequency Mode
Phase/Time difference mode
Statistical analysis

## Slide 12: Frequency Modes
What is the frequency mode
How does is operate
What may it be used to measure
Set-up files
What are the advantages of this mode

## Slide 13: Phase/Time difference mode
What is the Phase/Time difference mode
How does it work operate
What it be used to measure
Set-up files
What are the advantages of this mode

## Slide 14: Stable 32 frequency stability analysis
What is it
What can it do
How does it work
Who else uses it

## Slide 15: Statistics used for T&F calibration
Fractional Frequency Offset
Mean Fractional Frequency Offset
Allan Variance
Modified Allan Variance
Time Variance

## Slide 16: Characterisation of the A7
How to Characterise the unit- method and equipment
Expected results in freq. and phase mode
Data collection and analysis
Results- STS, drift and rms. resolution
Short Term Stability 1s ~5.5E-14 10s ~8.5E-15 100s ~1.3E-15 1000s ~1.6E-16 10000s ~2.6E-17
Drift ~2E-17/d
Drift/C ~2ps
rms. Resolution 0.3ps

## Slide 17: Plot of Tests done at USNO


## Slide 18: Benefits & Applications
Best commercial frequency measurements
Off the shelf solution enables relative novices to perform top level calibrations
May test ALL commercial frequency standards in fastest possible time
Modular design & powerful post-processing enable metrologist to configure to own need

## Slide 19: Users (so far!)
Korea - Hyundai.
Czech Republic -Mea test.
Quartzlock.
Bulgaria - National Standards Laboratory.
British Airways Engineering
Interlab (Poland)
USNO/Geodetic survey of Canada ?

## Slide 20: The Future
Further integration of CIS physics capabilities w/ modern western electronics
Penetration of unit into defence and telecom
Development of new unit with lower noise floor, higher resolution, lower noise floor, western phase comparator and wider range of input frequencies.
Adaptations of unit for specific customers

## Slide 21: Conclusion
Modular construction > suits all needs
Unique high resolution and stability measurement solution for T&F Metrology
Multiple modes and characterisation post processing options empower user
further work should produce even more user friendly and adaptable unit Watch this Space !!