## Slide 1: Craft Alpha 1
Development Of A New Reference Clock For Telecommunications And Calibration
Richard Percival, Clive Green and Mark Rainer

## Slide 2: Introduction to CRAFT
European commission money to develop primary reference clock for Telecoms
Top level clock not primary frequency standard
Combines resources and expertise of several European SME’s
24 month duration. Start date march 2000

## Slide 3: Companies Involved
Quartzlock (UK) ltd- project coordinator
K&K Gmbh (D)- software development
Simek, Cathodean, Eltek and Menvier hybrids- thick/thin film technology, scientific glass blowing, magnetic shielding & ceramic substrate hybrids
Mark Rainer, RF solutions & Farran – h-maser and rubidium electronics, GPS and LF TX RX
PTB- primary research work

## Slide 4: Goal 1: ALPHA 1
High-level redundancy (unlimited) by modular arrangement
Limitless generator connection
Cellular division ability in the event of a crisis
Hot swap capability with zero transients,
Nodal connection arrangement,
Inter-node communication ensuring robust operation and improved system integrity and security

## Slide 5: Goal 2: ALPHA 1
Excellent short, medium and long term stability.
Enable standards of different performances to be combined to effectively.
International traceability to highest levels.
Use of multiple satellite systems ensures system strategic independence of clock.
Contribute to deeper understanding of wall shift problem in h-maser.

## Slide 6: Different Elements of Project
Passive hydrogen maser
Lf tracking receiver
Rubidium
Microwave satellite receivers
Software clock
Measurement system
Time transfer
Other

## Slide 7: Passive Hydrogen Maser
Modernize and Globalise electronics
Package to appeal to Telecoms and non-metrology users & reduce size
Incorporate IRIG-B and RS232 more effectively to enable PC monitoring of health status and timing
Continue work on understanding fundamental physics limitations
Improve performance in both time and frequency domains

## Slide 8: Lf Tracking Receiver
Use of microprocessor enables synthesizer to be used > multiple input carrier frequencies
One instrument that works on MSF, DCF 77, France inter, WWVB and other LF transmissions
Digital filtering techniques will allow longer time constants thus improving medium term stability
Thermal stability to be improved by reducing bandwidth of receiver to <1 Hz. Removes need for narrow band tuned circuits
Performance limiting factor should be LO quality

## Slide 9: Rubidium
Increase the reliability and environmental stability
Make progress towards extending lifetime of lamp
Increase the range (ambient) over which the unit may perform to -65 deg C to +65 deg C, with a potential base plate temperature of over 90deg C
Enclosure of ~220cc has been proposed with a potential for 150cc version with OCXO footprint

## Slide 10: Microwave Satellite Receivers
Reason for inclusion is to improve the long term stability of PRC > Cesium derived long term stability and improve accuracy of PRC
Improvement will be made in the software packages to algorithmically weight the satellite information
Integrate a 24-channel dual system GPS/Glonass/Galileo engine that has full EGNOS and WAAS capabilities
Temperature controlling of the downconvertor & Antenna

## Slide 11: Time Transfer
1ns resolution with an accuracy of at least 5ns.
Inputs will be a 1pps of the PRC and a reference 1pps from a common view GPS receiver.
Software employed will enable automatic tracking of the BIPM schedule > Autonomous operation of the module, with automatic satellite selection and data collection.
Create cost-effective method ensuring traceability for clock to highest international authorities.

## Slide 12: Software Clock 1
A phase aligning interface module enabling the coupling of each clock to the interconnecting lines
A measurement system that enables clock drift to effect weighting in the algorithm that realizes averaging of clocks in a robust system
Innovative element of the clock
Combine a (considerable) number of diverse frequency standards so as to result in a single time-scale

## Slide 13: Software Clock 2
Random behaviour of the output phase of a source should be detectable by comparison with the phase of the other sources.
Derive a notional time scale based on phase measurement of all the sources and phase-align all the sources to the notional time scale.
Develop computer algorithms used to derive the notional time scale.
Assess importance of noise in phase aligners.

## Slide 14: Simplified PRC Diagram

## Slide 15: Measurement System
Development of a new Phase Comparator to be used for determining clock drift and deciding weighting of different clock elements.
System dedicated solely to measurement.
Wideband frequency input range (2048 kHz, 13 MHz, 1544 kHz may be used).
Improve sampling resolution to ~ 1000Hz in phase mode (Allan Variance <1s possible).

## Slide 16: Conclusion
Reliability for time standards of all kinds whether for standard laboratory calibration, Telecom Network Synchronization at the Stratum 1 level or national standards laboratories.
User-friendly system, with the modular structure enabling customer choice and cost flexibility, ease of service and the ability to upgrade when required.
Extreme reliability will be derived by virtue of multiple redundancies with all processing being accomplished in a distributed fashion.