## Slide 1: Move the Modular Force
For additional information or to help clarify information on a slide, select View and then drop down to select Notes Page.
Notes: FM 4-90.1, para 6-93: Tactical vehicles are the backbone of the support structure. They are mobile, flexible, and reliable. The transportation platoon of the BSB’s distribution company and the transportation sections in the maneuver units’ FSCs and the equipment mix for an operation depend on METT-TC. Planning factors include the planned flow of personnel and materiel and the availability and quality of the road networks. The right tactical trucks, in the right place, at the right time are essential to the success of any military operation.
Transportation is a fairly easy logistics function to plan for, but fairly difficult to execute. Consider the lessons learned from OEF I thru OEF IV in Afghanistan and OIF I thru OIF III in Iraq:
Afghanistan. Moving the force was exceptionally difficult in Afghanistan. For OEF I and II, all U.S. and coalition equipment arrived in theater by air. Some equipment was provided by host-nation and neighboring-nation support. CL IV was moved from Pakistan. CL III (B) was moved by ground. Even today, U.S. forces move only minimal amounts of supply by ground—the majority of surface transportation outside the wire is contracted for. This leads to pilfered loads, inability to conduct ITV, etc.
Iraq. For OIF I and II, units crossed LD w/ UBL and some organic equipment. Due to (1) a shortage of transportation assets, (2) unsecured lines of communications (LOCs), and (3) a disproportionate amount of personnel, equipment, and supplies coming into theater, anything left in Kuwait was subject to a prioritization flow north. The result -- some units waited months for any equipment that didn’t LD with them.
88M. For OIF, unarguably 88M is among the most dangerous MOS to hold, given that 95% of hostile action was directed at softer-skinned resupply convoys laden w/ CL III, CL IX, bottled water, etc.

## Slide 2: TLO and ELOs
Terminal Learning Objective: Describe mission support capabilities of the modular transportation force and operational considerations for employing transportation modes to support operations
Enabling Learning Objectives:
Identify the missions, capabilities, and employment of HBCT and sustainment brigade transportation elements
Identify considerations for planning ground transportation support and the interface of transportation planners, managers, and mode operators
Identify procedures for estimating transportation requirements to support the concept of operations

## Slide 3: References
FMI 4-90.1, Heavy Brigade Combat Team Logistics (Mar 05)
FMI 3-90-6, Heavy Brigade Combat Team (Mar 05)
FM 4-93.2, The Sustainment Brigade (Cord Draft Oct 05)
FM 4-0, Combat Service Support (Aug 03)
FM 4-01.011, Unit Movement Operations (Oct 02)
FM 4-01.30, Movement Control (Sep 03)
FM 4-01.41, Army Rail Operations (Dec 03)
FM 4-20.41, Aerial Delivery Distribution in the Theater of Operations (Aug 03)
Notes: These FMIs are primary emerging doctrinal sources for logistics support of the Modular Force:
  FMI 4-90.1, Heavy Brigade Combat Team Logistics
  FMI 3-90-6, Heavy Brigade Combat Team
  FM 4-93.2, The Sustainment Brigade
The following FMs are still considered primary doctrinal sources by the U.S. Army Transportation Center and School:
  FM 4-01.011, Unit Movement Operations
  FM 4-01.30, Movement Control
  All 55-series FMs

## Slide 4: References (continued)
FM 55-30, Army Motor Transport Units and Operations (with Change 1 Sep 99) (Pending revision FM 4-01.40)
FM 55-50, Army Water Transport Operations (with Change 1, Mar 95)
FM 55-60, Army Terminal Operations (Apr 96)
FM 55-80, Army Container Operations (Aug 97)
FM 100-17, Mobilization, Deployment, Redeployment, Demobilization (Oct 92)
Note: FM 55-50, -60, & -80 are pending revision to FM 4-01.50
Notes: Logistics FMs are being revised as FM 4 series manuals.
Note that a revision, FM 4-01.40, is being developed to supersede FM 55-30.
Note also that the following three FMs: FM 55-50, 55-60, and 55-80 will be revised as one series 4 FM, FM 4-01.50.

## Slide 5: Outline
Transportation Terms, Levels, Principles, & Concepts
Transportation Planners and Managers
Transportation Units, Missions, & Employment
Transportation Movement Requests (TMR)
Movement Control
Transportation Automation and Enablers
Aerial Resupply
Planning Considerations for Offense, Defense, and Urban Operations
Questions and Lessons Learned Discussion
Notes: Here’s the outline for this overivew on transportation support of a modular force.
The first few slides provide a big-picture familiarization of basic terms and concepts.
Starting with the Trans Units, Missions and Employment section, the slides are geared toward helping you obtain basic familiarization to plan transportation support, as well as to prepare you to coordinate transportation support for the Modular Force and the Iraqi theater of operations.

## Slide 6: Modular Force Acronyms (Move-specific)
BCS3: Battle Command Sustainment Support System
BSA: Brigade Support Area
BSB: Brigade Support Battalion
CABSA: Combined Arms Battalion Support Area
CHU: Container Handling Unit
CROP: Container Roll in / Roll out Platform
DC: Distribution Company
FBCB2: Force Battle Command Brigade and Below
FDRP: First Destination Reporting Point
FRCP: Flatrack Collection Point
FSC: Forward Support Company
ITV: In-transit Visibility
LHS: Load Handling System
MTS: Movement Tracking System
PLS: Palletized Load System
SA: Situational Awareness

## Slide 7: Move the Modular Force
Transportation Terms, Levels, Principles, & Concepts

## Slide 8: Transportation
Transportation is moving and transferring units, personnel, equipment, and supplies to support the concept of operations.
Transportation incorporates military, commercial, and host-nation capabilities.
Transportation assets include:
  Motor, rail, air, and water modes and units
  Terminal units, activities, and infrastructure
  Movement control units and activities
Notes: (Reference: FM 4-90.1, pg 5-27, para 5-109)
Experience in Afghanistan and OIF will help to illustrate the second bullet on this slide:
  Afghanistan: There was/is some military ground movement, but this AO has significant host nation and neighboring nation (Pakistan) transportation support.
  OIF: There was/is lots of military ground movement, but also tons of host nation transportation support. For OIF-1, specifically for the period from MAY 03 thru FEB 04, the 101st Airborne Division (AASLT) employed 125 host nation drivers and contracted up to 63 tractor-trailer combinations just at division level to supplement the division transportation company. Each FSB employed additional drivers and tractor-trailer combinations to give them an “organic” host nation transportation capability.

## Slide 9
Levels of Transportation
Strategic Level
  Focus is on the movement of U.S. forces and equipment to SPOEs and from SPODs
  U.S. Transportation Command (USTRANSCOM) controls strategic movement through its three component commands:
    Surface Deployment and Distribution Command (SDDC) (formerly known as MTMC)
    Air Mobility Command (AMC)
    Military Sealift Command (MSC)
Notes: USTRANSCOM Mission: (Reference: FM 4-0, pg. 7-2, para. 7-1)
SDDC Mission: Provides global surface deployment command & control and distribution operations to meet National Security objectives in peace and war (Reference: FM 4-0, pg. 7-1, para. 7-2)
AMC Mission: Provides common-user airlift, air refueling, and strategic aero-medical evacuation transportation services to support U.S. forces on a global basis. (Reference: FM 4-0, pg. 7-2, para. 7-3)
MSC Mission: Provides government owned and government-chartered sealift transportation services to support U.S. forces globally. (Reference: FM 4-0, pg. 7-2, para. 7-4)

## Slide 10: Levels of Transportation
Operational Level
  Focus is on building force structure; reception, staging, and onward movement; opening ports; establishing LOCs; and providing C2 for movements.
Tactical Level
  Focus is on supporting the commander’s intent (right support, right place, right time).
Notes: (Reference: FM 4-0, pg. 7-2 to 7-3, para. 7-8 and 7-9)

## Slide 11: Basic Movement Control Principles
Centralized control/decentralized execution
Regulated movement
Fluid and flexible movements
Effective use of carrying capacity
Forward support
Transportation System Elements
Movement Control (most important element)
Mode Operations
Terminal Operations
Notes: <number>
<header>
(Reference: FM 4-01.30, pg. 1-1, para. 1-2 and pg. 1-2, para. 1-3) The transportation system is comprised of three distinct elements: mode operations (highway, rail, water, air), terminal operations, and movement control.
Movement control is the most critical component of the system (and it will be addressed in depth later in the lesson). Movement control organizations/teams must coordinate the efforts of modes, terminals, services, commands, contractors, and host nations during deployment, sustainment, and redeployment.
Mode Operators. Include drivers and equipment operators. Provide transportation assets as committed. Operate trailer transfer points (TTPs) and inland terminals. Our mode focus in this lessonI is predominately on motorized operations
Basic Movement Control Principles are still in effect despite the transition from AOE to Modular Force emerging doctrine. It is not clear yet whether or not the se basic principles will be reworded, expanded, combined, etc. in the future to account for this and other emerging Modular Force doctrine
Centralized Controll: Planning and resource allocation for current and future requirements is executed by planners and managers at each level of command involved in an operation.
Decentralized Execution: Mode operators determine the specific assets to assign to meet the requirement.
Regulated Movement: Prevent conflict/congestion by avoiding system saturation. Three applications: Apportionment of Vehicles to Requirements, Regulation of Traffic thru MSRs and LOCs, and Force Projection. Command priorities guide the regulation of all movements.
Fluid and Flexible Movements. Uninterrupted movement of personnel, supplies, and services is critical. System must allow for traffic re-routing and diversion. System must be linked to Situational Awareness (SA) systems to maximize movement control.
Effective Use of Carrying Capacity. Make the best use of your available assets. Empty trucks sitting idle benefit no one. When the mission is complete, return the asset so it can be fully utilized. Keep assets fully loaded and moving. Select the best platform for a given load. Requesting units must be disciplined and return corps, division, and BSB assets when their mission is complete.
Forward Support. Support forward to provide maximum responsiveness to the maneuver commander. Rapid delivery of supplies and personnel as far forward as possible. Dependent upon fast, reliable transportation. Rapid reception of assets (receive, download, and clearance/release). May be necessary to augment destination unit’s reception and clearance capabilities (pre-stage a forklift to help the destination unit download pallets from a corps medium truck company).
Additional principles specific to the Modular Force are covered on the next slide.

## Slide 12
Unity of Command, Centralized Distribution Management -- The movement control NCO in the BSB support operations section performs this function for the HBCT.
Increased Velocity, Throughput to Forward Areas -- The BSB SPO maintains constant ITV of sustainment resupply convoys entering the HBCT boundary. The movement control NCO in the BSB SPO maintains constant ITV of all sustainment resupply convoys in/out of the BSA through movement tracking system (MTS).
Increased Velocity, Minimize Load Handling --Minimizing load handling of cargo and reducing materiel handling equipment requirements are essential to successful throughput to forward areas.
Movement Principles in the HBCT
Notes: (Reference: FM 4-90.1, pg. 6-24, para. 6-104 to 6-106)
These additional principles are described in FMI 4-90.1. They apply specifically to efforts to provide transportation support to the HBCT (Modular Force).
Unity of Command/Centralized Distribution Management. This principle is focused on synchronizing movement and maintaining visibility of assets. The unity of command piece is encompassed by everybody on the battlefield (to include the war-fighters) understanding that the Modular Force is attempting to move mountains with limited assets. Understanding this, movement guys give 100% to supporting and war-fighters and 100% to downloading and returning assets quickly. To keep the system honest, trans officers at the BSB (the trans officer and the trans management NCO) maintain visibility on all assets requested, required, and being sent to their HBCT’s AO.
  If a unit attempts to hold an asset, the BSB takes action.
  If a unit needs an asset to facilitate download (forklift), the BSB takes action quickly.
  If a unit is feverishly awaiting arrival of a specific load, the BSB tracks that load/asset using MTS, FBCB2, and BCS3 enablers.
Increased Velocity, Throughput to Forward Areas. Bypass one or more echelons in the distribution network to minimize cargo handling and improve velocity on the battlefield.
ITV is maintained thru MTS, FBCB2, and BCS3 (SA systems). Direct throughput relies on: unity of command and situational understanding.
Increased Velocity, Minimize Load Handling. Use PLS, HEMTT-LHS, and CROP to reduce handling requirements forward on the battlefield. These systems extend throughput capability and enhance velocity through flatrack exchange at or near the BSA and the CABSAs.

## Slide 13: Flatrack Management
Flatrack employment, management, and retrograde operations are the responsibility of distribution managers integrated at each echelon of support throughout the HBCT area.
Flatracks will be dispersed throughout the distribution pipeline, particularly from the HBCT rear boundary to the combat trains command post (CTCP) of a combat battalion or dispersed throughout the area of operation.
Flatrack exchange is the preferred method for retrograding flatracks from the CABSA. The Flatrack Collection Points (FRCPs) are designated for flatrack consolidation purposes when required. Proposed locations are reported to the BSB support operations officer.
Notes: Reference: FM 4-90.1, pg 6-25-27 highlights flatrack management at the BN/Squadron Support Area as well as at the BDE Support Area.
In the brigade area and below, flatrack managers include the:
  FSC Distribution Platoon Leader, FSC Executive Officer, BSB SPT OPS Movement Control NCO, and the Trans Platoon Leader (from the BSB’s Distribution Company)
FM 4-90.1, pg. 6-27, 6-113 and 6-120 lists their responsibilities as:
Identifying a proposed flatrack collection point (FRCP) ICW the BSB DC transportation platoon leader.
Managing all common user flatracks on an area basis.
Ensuring flatrack exchange procedures are optimized using division throughput assets as a matter of priority.
Maximizing the use of BSB DC transportation LHSs for retrograding/back hauling flatracks from the FRCP back into the distribution pipeline.
Reporting flatrack on-hand quantity by location, status, and condition to the Transportation Branch (MCO) at the Division.
Coordinating with the Division Transportation Branch for supplemental transportation support when retrograding flatracks from BSA FRCP.

## Slide 14: Move the Modular Force
Transportation
Planners and Managers
Notes: FMI 4-90.1, para 6-104: Synchronizing movement and materiel management, and maintaining integrated end-to-end visibility of transportation assets, is key to the successful operation of an efficient, fully integrated transportation system at the HBCT level.
The movement of the brigade is coordinated and synchronized with the HBCT S3 and S4.
The brigade S3 manages and approves all tactical movements in the brigade’s battlespace. The brigade S3 must also monitor that all logistics movements are synchronized with the scheme of maneuver.
The brigade S4 plans, manages, and monitors all logistics movements with the BSB support operations.
The BSB support operations office (SPO) manages and executes the movements and maintains visibility through MTS.
Note: The slides that follow for planners and managers will be modified in the coming months as doctrine continues to emerge. No definitive relationship is spelled out above the BSB level in any of the FMs. However, pieces and parts of emerging doctrine have been coupled with insight taken from personnel at Fort Stewart and Fort Campbell to attempt to neatly link planners, managers, and the transportation request process.

## Slide 15: Planners, Managers and Key Tasks
XX
TSC
SUST
X
CTC
MED
Sustainment
Base
SPO/DMC
Plans
Ops
Trans
Med
HR Ops
FM Ops
SUST
BDE
X
S&S Cell
Ammo Cell
SPO
BSB
Maint Cell
Trans Mgmt Cell
HSS Cell
Contract Cell
Dist
FSC
PLT HQ
CL III Section
CL V
Gen Supply Sec
Trans Section (IBCT only)
Dist
CO HQ
Supply PLT
Fuel / H20 PLT
Trans PLT
Key Task
Maintain ITV
Task Sustainment Brigades
Execute throughput
Key Task
Maintain ITV
Execute taskings received from TSC to support one or more Division’s.
Key Task
Maintain ITV
Task assets within the DC to execute requirements.
Pass requirements that exceed capability to TSC.
Key Task
Maintain ITV
Execute taskings received from Trans Mgmt Cell (SPO)
Key Task
Maintain ITV
Use CULT assets to execute trans requirements (HBCT)
    Trans Section moves one company in one lift (IBCT)
Key Task
BN S4 consolidates requirements and passes to FSC
Division Trans Officer
MCB
Notes: References for this slide are listed individually on the slides that follow. This is just a roll-up.
A CULT asset is nothing more than a traditionally non-taskable asset that can be downloaded and tasked to perform a transportation mission.
Examples:
  FMTVs in the FSCs that are on MTOE to carry life-support equipment.
  A lowboy in the BSB (the MTOE intent for the lowboy is to move BSBs forklifts)—it may be tasked as a CULT asset to move something else for a requesting unit (FMI 4-90.1, pg. 6-22, para 6-93 thru 6-95.

## Slide 16: Brigade Support Battalion, HBCT
Maint Cell
Sup & Svc Cell
Trans Mgt Cell
HSS Cell
Ammo Cell
Contract Cell
SPO
Field Maintenance
Company
Distribution
Company
Medical
Company
BSB
BSB
Notes: Reference: FMI 3-90.6, pg. 10-3, Figure 10-1
The BSB is structured with SOME organic transportation assets to meet the maneuver BCT’s sustainment support requirements.
FM 4-90.1, para 6-109. The BSB support operations office assumes the distribution management center’s role in providing continuous and responsive sustainment to the brigade through a variety of STAMIS and the BCS3 managed by the section. The BSB’s limited distribution capability relies heavily on support from the division for sustainment throughput. The BSB’s distribution manager synchronizes the delivery schedule with customer units and transfers information between the brigade S4 and the battalionS4/FSC (via MTS) to schedule and synchronize transportation requirements within or in direct support of brigade or battalion operations. For supplemental transportation support and coordination on inbound and outbound shipments the BSB movement control NCO coordinates with the division through MTS.
The Transportation Management Cell at the BSB consists of the trans officer (03 / 88A) and the trans management NCO (88N20). They maintain visibility on all assets requested, required, and being sent to their HBCT’s AO.
If a unit attempts to hold an asset, the trans management cell takes action.
If a unit needs an asset to facilitate download (forklift), the trans management cell takes action quickly.
If a unit is feverishly awaiting arrival of a specific load, the trans management cell tracks that load / asset using MTS, FBCB2, and BCS3 enablers. (FMI 4-90.1, pg. 6-24, para. 6-104 thru 6-106)

## Slide 17: Support Operations (BSB)
SPO: Principal staff officer (ICW S1, S4, and Surgeon) for logistics support to the HBCT.
Note: The S4 is the HBCT Logistics Officer. The S4 and SPO work closely together to support the HBCT.
Transportation Management Cell (shown on previous slide):
    Coordinates/monitors all transportation movements for the BSB.
    Coordinates backhaul of equipment ICW the Transportation Branch.
    Consists of two traffic management coordinators assigned to control the movement of assets in and around the BSB.
Notes: FMI 4-90.1, pg. 3-20, para. 3-76 and pg. 3-15, para. 3-51 thru 3-53
The SPO provides supervision for the BSB’s external log missions. He is the key interface between the supported units and the BSB. He works with the HBCT’s S1, S4, Surgeon, and the log reps (S4s, S1s, FSC Commanders) from each of the supported units. The SPO requests and coordinates augmentation when requirements exceed capabilities (para. 3-76).
The traffic management cell uses its two traffic management coordinators to control the movement of assets in and around the BSB. They coordinate, monitor, control, and supervise the movement of personnel, equipment, and cargo by air, rail, highway, and water and determine which of those modes is most efficient to accomplish mission requirements.
  When trans requirements exceed capability, the traffic management coordinators coordinate support with the MCO in the Sustainment Brigade’s SPT OPS section.
  The also anticipate the need for utilization of MSRs and may recommend primary and alternate MSRs in their AO to the MCO.
  Additional responsibilities include maintaining ITV (MTS, FBCB2, BCS3).

## Slide 18: SPO Traffic Management Coordinators
Traffic Management Coordinators Duties:
  Coordinate, monitor, control, and supervise the movement of personnel, equipment, and cargo via air, rail, highway, and/or water.
  Determine the most efficient mode of transport that accomplishes mission requirements.
  Supervise cargo documentation and movement control for all transportation modes.
  Develop and review movement programs (to include convoy planning) for logistics support functions within the BSB/BSA.
Notes: FMI 4-90.1, pg. 3-15, para. 3-51 thru 3-54

## Slide 19: SPO Traffic Management Coordinators
Traffic Management Coordinators Duties (continued):
  Advise in the preparation of support plans where transportation is required.
  Verify the accuracy of movement control documents.
  Ensure allocation of transport capability is appropriate to accomplish each mission in a cost-effective manner.
  Coordinate support with the Transportation Branch in the sustainment brigade’s support operation section.
  Anticipate and recommend the use of main supply route (MSR) to the Transportation Branch.
Notes: FMI 4-90.1, pg. 3-15, para. 3-51 thru 3-54

## Slide 20: Movement NCO
Movement NCO Duties:
  Conduct continuous logistics preparation of the theater.
  Conduct overall flatrack management within the brigade support area.
  Prepare battalion movement plans and annexes in support of logistics or contingency plans.
  Resolve movement priority conflicts with the support operations officer and S2/S3.
Notes: FMI 4-90.1, pg. 3-15, para. 3-54
The movement control NCO has flatrack management and status reporting responsibility to the MCO.

## Slide 21: Movement NCO
Movement NCO Duties (continued):
  Coordinate subordinate unit movement requirements with EAB.
  Regulate MSR use requirements for unit moves.
  Operate movement tracking station.
  Coordinate movement of aerial logistics resupply.
Notes: FMI 4-90.1, pg. 3-15, para. 3-54

## Slide 22: Transportation Plt Ldr, DC, BSB
Transportation Platoon Leader:
  Works for Distribution Company Commander.
  Receives taskings from the BN SPT OPS Section.
  Provides transportation support for the distribution of supplies to FSCs.
  Provides transportation to Bde using 20 x PLS.
Co HQ
FUEL/
WATER
PLT
TRANS
PLT
SUP PLT
DISTRO
Focus:
  Conduct resupply LOGPACs to the FSC's distribution assets for their LOGPAC operations and receive resupply from corps/division.
Notes: FMI 4-90.1, pg. 3-27, para. 3-98 thru 3-101 and pg. 6-22, para. 6-93 thru 6-95
Using 20 x PLSs, the transportation platoon provides direct transportation support to the HBCT and distributes supplies to the FSCs. The PLSs provide a mobile, flexible, and reliable capability.
The transportation platoon may mix its assets with some common –user land transport (CULT) assets within the FSCs to accomplish a mission based on METT-TC.

## Slide 23: FSC Distribution Platoon (HBCT)
Distribution Platoon Leader:
  Executes transportation missions for their respective battalions.
BN S4:
  Consolidates support requirements and passes them to the FSC CP for execution by the distribution platoon.
  Coordinates with the BSB support operations section for additional assets if required.
  Note: Info is also passed to the BDE S4 for SA/ITV.
Dist
CL III
Section
CL V
Gen Sup
Section
Plt HQ
FSC
Trans
Section
IBCT only
Notes: FMI 3-90.5, pg. 10-14, para. 10-45
FMI 4-90.1, para 6-110. The FSC CP assumes the movement and materiel management and maintenance (evacuation) functions as the lowest echelon of transportation support to a BN/SQDN. The FSC CP coordinates with the BN S4 and synchronizes the delivery of all classes of supply with customer units and transfers requirements and capabilities to the BSB support operations. The FSC CP schedules and synchronizes transportation support and coordinates inbound and outbound shipments with the BSB movement control NCO through MTS.

## Slide 24: Planners, Managers and Key Tasks Review
XX
TSC
SUST
X
CTC
MED
Sustainment
Base
SPO/DMC
Plans
Ops
Trans
Med
HR Ops
FM Ops
SUST
BDE
X
S&S Cell
Ammo Cell
SPO
BSB
Maint Cell
Trans Mgmt Cell
HSS Cell
Contract Cell
Dist
FSC
Division
PLT HQ
CL III Section
CL V
Gen Supply Sec
Trans Section (IBCT only)
Dist
CO HQ
Supply PLT
Fuel / H20 PLT
Trans PLT
Key Task
Maintain ITV
Task Sustainment Brigades
Execute throughput
Key Task
Maintain ITV
Execute taskings received from TSC to support one or more Division’s.
Key Task
Maintain ITV
Task assets within the DC to execute requirements.
Pass requirements that exceed capability to TSC.
Key Task
Maintain ITV
Execute taskings received from Trans Mgmt Cell (SPO)
Key Task
Maintain ITV
Use CULT assets to execute trans requirements (HBCT)
    Trans Section moves one company in one lift (IBCT)
Key Task
BN S4 consolidates requirements and passes to FSC
Division Trans Officer
MCB
Notes: Review one last time.

## Slide 25
Transportation
Units, Missions, & Employment
Move the Modular Force
Notes: FM 4-90.1, para 6-94: Each echelon centrally controls common-user transport assets to respond to their unit commander's priorities and weight the logistics effort. At HBCT level, the BSB provides transport support under control of the BSB support operations. The HBCT’s transportation units can expect to move frequently in response to changes in requirements. FM 4-01.30 has detailed information on transport units and operations.
NOTE: WEBTAADS, CASCOM Force Development Doctrine, and MTOEs for 3ID, 101st, and various other units, still show Heavy Truck Companies, Medium Truck Companies, and Light/Medium Truck Companies available. An updated description of capabilities and equipment for these units follows in the Transportation Units, Missions, and Employment section of this lesson. Force Developers within CASCOM have noted that some transportation units may be “massaged” as the Modular Force continues to evolve.
None of the FMs identify exactly what units will be found at the corps and division area (although FMI 4-90.1, pg. 6-6, Figure 6-2 identifies dry cargo associated with a transportation company). Until FM 55-30 is replaced with FMI 4-01.40, we’re still using Medium Truck Companies (POL, PLS, Cargo), LT/MED, HET, and CTCs as the primary corps/division trans units on the battlefield.

## Slide 26: Sustainment Brigade
Mission: Plan, prepare, execute, and assess CSS operations within assigned AO.
CSSB
CSSB
CSSB
CSSB
CSSB
CSSB
SUS
BTB
HHC
SIG
CSSB
FIN
HR
AMMO
TRANS
MAINT
S&S
HHC
MFMB
Assigned
Attached
Attached
Assigned
Notes: Reference: Ch 11, Sustainment Brigade Organizational & Operational Concepts White Paper, pg. F-21
Note: The only organic element to the Sustainment Brigade is the Brigade Troops Battalion (BTB), indicated in blue above. The Combat Sustainment Support Battalion (shaded green) is tailored based on METT-TC and may consist of functional companies that provide supplies, ammo, fuel, transportation, maintenance, and field services
Highlighted is a functional transportation company under a CSSB from the Sustainment Brigade.

## Slide 27: Heavy Truck Company
Mission: To relocate tracked combat vehicles in support of a heavy maneuver force. Configured in either 2 or 4 HET platoons.
Equipment:
2 Platoons
48 Tractors, HET
48 HET, Trailer 70 T
96 Tractors, HET
96 Trailers, 70 T
4 Platoons
Notes: <number>
<header>
FM 54-30, page 10-3; FM 63-3, page 8-10; and ST 101-6, page 3-50
The combat HET company’s primary role is to relocate tracked combat vehicles in support of a heavy maneuver force. Combat HET companies deploy in the early stages of theater buildup. Their evacuation role becomes secondary.
Relocating and transporting tracked vehicles to the battle on HETs provide a significant advantage over road marching tracked vehicles. Tracked vehicles arrive fully fueled, armed, and operational, with rested crews. Weapon systems arrive functional and less fuel is consumed.
Note: The basis of allocation is TBD.

## Slide 28: Medium Truck Company
Mission: To move bulk, containerized, general non-containerized cargo, and bulk POL from supply and stockage points to users.
Equipment:
Container/Cgo Container/Cgo POL PLS
60 trks, trac 5 T 60 trks, trac M915 60 trks, trac M915 48 PLS trucks
150 semitrlrs, 22 1/2 T 120 semitrlrs, 34 T 60 tankers, 5/7.5 K gal 48 PLS trlrs
96 flat racks
Notes: <number>
<header>
FMI 4-90.1, pg 6-6, 6-8, and 6-37; FM 54-30, pages 10-1 & 10-3; FM 63-3, page 8-10; and ST 101-6
NOTE: WEBTAADS, CASCOM Force Development Doctrine, and MTOEs for 3ID, 101st, and various other units, still show Heavy Truck Companies, Medium Truck Companies, and Light/Medium Truck Companies available. An updated description of capabilities and equipment for these units follows in the Transportation Units, Missions, and Employment section of this lesson. Force Developers within CASCOM have noted that some transportation units may be “massaged” as the Modular Force continues to evolve.
The Medium Truck Co is the work horse on the battlefield. There are four different equipment authorizations for medium truck companies. They move containerized or general cargo, bulk fuels, or refrigerated cargo.
Med Truck COs (Cargo): Employs near the TSC (specifically near the QSC). Transports general supplies (throughputs whenever possible) to the unit, pulses to the BSB, or delivers to the MSO site established by the Division Sustainment Brigade. Whenever possible, they retrograde or return loads from forward areas to the corps or division area. (FMI 4-90.1, pg. 6-6, para. 6-30)
POL Truck Co: Employs near and habitually supports the Petroleum Pipeline and Terminal Operating Company in the corps or the Petroleum Supply Company in the corps/division. Pushes fuel directly to BSB locations. (FMI 4-90.1, pg. 6-8, para. 6-42)
Med Truck COs (PLS): Forms habitual support relationships with GS/DS ammunition companies to transport munitions from the corps ASA to the division ASA and ATHPs designated for the HBCTs. (FMI 4-90.1, pg. 6-37, para 6-168)

## Slide 29: Light/Medium Truck Company
Mission: To move general and non-containerized cargo and personnel in support of corps and division units.
Equipment:
  50 x FMTV (M1083)
    25 x MTV Dropside Trailers (M1095)
  10 x Tractors (M1088)
    20 x 22 ½ Ton Semi-trailer (M871)
Notes: <number>
<header>
Reference: WEBTAADS (3ID and 101st for light Division comments)
Light/Medium Truck Companies will be found in the corps/division. They can fall directly under the Division Sustainment Brigade (as the 494th Trans Company falls under the 129th CSSB in Fort Campbell). They transport supplies from the QSC in the corps area to the Sustainment Brigade in the division and/or from the CSSB supply company to BSB main supply points.
Light/Medium Truck Companies also support maneuver brigade operations, moving troops or cargo as required.
  For troop movement, a light/medium truck company can be expected to accommodate transportation taskings in the division that exceed any of the FSCs capability (especially in light divisions).
  For heavy divisions, the light/medium truck company could be leaned heavily on to execute any troop movement mission that requires the use of multiple cargo trucks.
Light/Medium truck companies basis of allocation is TBD. For AOE, the basis of allocation was one per division.

## Slide 30: Cargo Transfer Company
Mission: To transfer cargo at air, rail, motor, and inland barge terminals.
Equipment:
16
4
KALMAR
Trac, M915
16
4
Semitrlr, 34 T
16
4
RTFL, 10 K
4
16
RTFL, 4 K
2
8
1 x Cgo Trf Plt
4 x Cgo Trf Plt
 | PLS | CHU | Crane (40T)
1 x Cgo Trf Plt | 2 | 1 | 1
4 x Cgo Trf Plt | 8 | 4 | 4
*Can operate in 1 x PLT or 4 x PLT configuration.
Notes: <number>
<header>
FM 54-30, page 10-3; FM 63-3, page 8-10; and ST 101-6 (Primary terminal operator)
Cargo transfer companies trans-ship cargo at air, rail, and motor terminals. They can be assigned to a corps or division. As an example, the 372nd CTC from the 101st Airborne Division is assigned to the Division Sustainment Brigade.
The CTC can operate in either a one or four-platoon configuration, depending on the unit authorization and a variety of other factors (availability of commissioned and noncommissioned leaders, maintenance status, etc.). Each platoon is organized to operate a terminal on a 24-hour basis.
Cargo transfer units are sequenced early in the deployment flow. They initially operate at arrival airfields, supporting combat units in the off-load and marshaling of unit equipment and unit supplies. As the operational area is expanded, cargo transfer units are echeloned forward to conduct cargo handling operations at forward mode transfer points and/or to augment division or corps operations with attached cargo handling elements tailored to the mission.
Unit personnel re-document transshipped cargo, as required. They have a limited capability for stuffing and unstuffing containers.
EQUIPMENT NOTES:
Container Handling Unit (CHU). The CHU is a PLS with special apparatus that allows grasping the front end of a 20-foot container, locking onto it and pulling the container onto the back of the CHU for movement around the battlefield. The CHU can take supply packages, such as a Class IX shipment, to the individual FSCs. Note: It does not involve the use of a flat-rack.
M915/M872s: Most CTCs still have these, however, these will be replaced by the PLS (Modular Force change). Once units are fielded PLSs, they will turn in the M915/M872s that they have remaining on their books.
KALMARs: Most CTCs have fielded the KALMAR; however, a few still have DV43 (50T RTCH). Units that still have the older RTCH still have 20’ and 40” spreaders on their property books as well.

## Slide 31: Heavy Brigade Combat Team
BSB
FSC
FSC
FSC
Notes: Reference: FMI 4-90.1, pg. 1-5, Figure 1-2
Trans PLTs (from the Distro Company in the BSB): Authorized 42 x 88Ms. Has 20 x PLS and a C2 vehicle.
  Note: There are also PLSs in the General Supply Section (3), CL IX Section (2), and the ATP Section (3).
Operators in the Trans Section of the FSC (light units only): In order to move troops when birds aren’t flying, the Trans Section in a light division’s FSC has 24 x 88Ms, 12 x LMTVs, and 8 x LMTV drop-side trailers. This section has the capability to move one company of infantry in one lift; (Reference: Ch. 11, White Paper, F-73, A.1.3, line 17-19)
ADDITIONAL NOTE: As of the 15 MAR 05 publishing of FMI 3-90.6 (see page 10-30, para. 10-90), the availability of HETs in the BSB has been removed from the previous draft. Bottom line: As of now, there is no HET capability at the BSB level and below.

## Slide 32: HBCT Brigade Support Battalion
TRANSPORTATION MISSION:
The Brigade Support Battalion (BSB) distributes supply Classes I, II, III, IV, V, VIII, and IX. It carries the sustainment stocks that exceed the organic carrying capability for the brigade’s three replenishment loads for high intensity operations.
Field Maintenance
Company
Distribution
Company
Medical
Company
BSB
BSB
Notes: Reference: Ch. 11, Sustainment Brigade Organizational & Operational Concepts White Paper, pg. F-72, A.1, line 5-11

## Slide 33: BSB Distribution Company
TRK SQD
Equipment:
20 x PLS
Notes: The BSB distribution company has 20 x PLS vehicles with trailers, though there are only two flatracks each for the vehicle and trailer instead of the previous AOE design with six. This internal capability allows them to conduct sustainment replenishment operations in support of the HBCT’s tactical mission and does not require the maneuver battalions’ FSCs to go to the BSA for sustainment replenishment, (FMI 3-90.6, pg. 10-29, para. 10-89)
The distribution company is assigned two drivers per platform, thus allowing the capability to provide 18 hour/7days a week pulse operations as required. (FMI 3-90.6, pg. 10-29, para. 10-89)

## Slide 34: Transportation PLT Mission, Distribution Co, BSB
Co HQ
FUEL/WATER
PLT
TRANS
PLT
SUP PLT
DISTRO
Provide direct transportation support to the brigade.
Provide distribution support of supplies to the FSCs.
Equipment:
  T93761 (Trailer: PLS) x 20
  T96496 (Truck: Cargo) x 20
Notes: Reference: FMI 4-90.1, pg. 3-27, para. 3-98 thru 3-101
The primary focus of the trans plt leader in a tactical scenario is conducting resupply LOGPACs to the FSC’s distribution assets for their own LOGPAC operations and receiving resupply from division/corps.
Although the trans PL works for the DC CDR, it receives taskings from the battalion Support Operations Section.
Trans PLTs (from the Distro Company in the BSB): Authorized 42 x 88Ms. Has 20 x PLS and a C2 vehicle.

## Slide 35: Distribution Platoon, FSC (HBCT/IBCT)
TRANS
SECTION
Move one company of infantry in one lift (IBCT).
FSC
Dist
HQS
Plt HQ
CL V
CL III
Section
Gen Sup
Section
Maint
Equipment (IBCT FSC):
12 x LMTV
8 x LMTV drop-side trailers
Equipment (HBCT FSC):
No doctrinally taskable truck assets; however, some movement missions may be executed using CULT assets.
Equipment:
12 x M978 Fuel HEMTT
1 x TPU w/ Trailer
Equipment:
5 x PLS w/ Trailers
2 x MTV w/ LMTV Trailers
Equipment:
2 x MTV
5 x LMTV
Notes: Reference: FMI 3-90.6, pg. 10-6, Figure 10-4 and Ch 11, White Paper, F-73, Line 16-19
Operators in the Trans Section of the FSC (light units only): In order to move troops when birds aren’t flying, the Trans Section in a light division’s FSC has 24 x 88Ms, 12 x LMTVs, and 8 x LMTV drop-side trailers. It has the capability to move one Infantry Company in one lift. (Reference: Ch. 11, Sustainment Brigade Organizational & Operational Concepts White Paper, pg. F-73, para. A.1.3, line 17-19)

## Slide 36: Employment (Modular Move)
Modularity Support Concept
Throughput
Modular Units/Capability
Sustainment
Base
Division
SUST
X
I
FSC
BSB
II
BSB
II
BSB
II
I
FSC
I
FSC
I
FSC
XX
TSC
SUST
X
CTC
LT/MED
MED
POL
HET
DC
DC
DC
Corps
MCB
Notes: Reference: Ch. 11, Sustainment Brigade Organizational & Operational Concepts White Paper, pg. F-32
Note: None of the FMs identify exactly what units will be found at the corps and division area (although FMI 4-90.1, pg. 6-6, Figure 6-2 identifies dry cargo associated with a transportation company). Until FM 55-30 is replaced with FMI 4-01.40, we’re still using Medium Truck Companies (POL, PLS, Cargo), LT/MED, HET, and CTCs as the primary corps/ division trans units on the battlefield.
Throughput. Direct throughput of supplies from the sustainment base and the HBCT to the combat battalions is the rule rather than the exception with distribution-based logistics.
Sustainment Bde CSSB. At the operational level, the CSSBs transportation assets will operate between the theater and the tactical sustainment brigade when loads can not be throughput to the BSBs. At the tactical level, the CSSBs transportation assets will provide mobility from the CSSB base to the BSB and the FSCs within the BCT area.
BSB Distribution Company. The BSB distribution company pushes supplies forward to the FSC where they are received by the Class III (bulk), transportation, and general supply sections. Load handling system (LHS), palletized load system (PLS) and heavy expanded mobility tactical truck (HEMTT) fuel tankers transport supplies via combat logistics patrols from the combat battalion’s support area i.e. the field train’s location to a battalion logistics release point (LRP) under the control of the FSC distribution platoon leader.
The FSCs in the battalions are the cornerstone of the distribution-based logistics system.

## Slide 37: First Destination Report Point
The FDRP is a point established near a boundary or along a MSR that diverts drivers and cargo to an alternate consignee or destination
Although the HBCT is digitized, a FDRP is routinely required since other supporting units, host nation elements, and/or contractors lack digital equipment
The FDRP is manned by a movement regulating team, a movement control team, or military police
Optimally, both the HBCT and supporting EAB headquarters have representatives located at the FDRP continuously
Notes: Reference: FMI 4-90.1, pg. 6-25, para. 6-111 thru 6-112
FMI 4-90.1, papa 611: The FDRP is a point manned by a movement regulating team, a movement control team, or military police that diverts a driver and cargo to an alternate consignee or destination. Basically, FDRPs are logistical information checkpoints.
Optimally, both the HBCT and supporting EAB headquarters have representatives located at the FDRP continuously. Security arrangements, command and control, and communications support must be addressed prior to FDRP establishment. Further amplification of FDRP operations can be included in unit SOPs. Some tasks performed at the FDRP are below:
  􀁺 Track location of critical supplies.
  􀁺 Perform movement control functions.
  􀁺 Provide instructions to convoys.
  􀁺 Provide and receive latest intelligence.
  􀁺 Reroute convoys/vehicles.
  􀁺 Provide information on routes and weather.
  􀁺 Establish brigade "light line" for black-out driving.
  􀁺 Linkup point for armed convoy escort vehicles.
Best example of a FDRP being used in OIF right now is NAVSTAR, just south of the Iraq border in Kuwait (south of Basrah).

## Slide 38: Move the Modular Force
Planning
Considerations for Offense, Defense, and Urban Operations

## Slide 39: Supporting Offensive Operations
Upload as much as possible
Reduce vulnerability of “thin-skinned” vehicles
Extended supply lines increase delivery and turn around times
Maximize use of preplanned and preconfigured push packages
Use airlift resupply for units not accessible by surface transportation.
Notes: FM 54-30, pages 10-11 and 10-12 (Validate)
Offensive Operations:
Forward delivery results in large numbers of transportation assets far forward in the division area.
Cargo vehicles, petroleum tankers, and ammo carriers are thin-skinned vehicles, vulnerable to small arms fire. Small enemy ground or air forces can easily decimate transportation assets.

## Slide 40: Supporting Defensive Operations
Delivery and turnaround times decrease
Supplies are moved to successive defensive positions
Ammunition expenditures and barrier materials increase, while fuel decreases

## Slide 41: Supporting Urban Warfare
Movement control is more complex
Civilian foot / vehicle traffic may interfere with operations.
Routes within an urban area can be denied easily
Force protection of logistics nodes and convoys is more difficult in urban areas (3-levels to worry about)
Smaller resupply vehicles (HEMTT/PLS) may be in greater demand than tractor-trailers
Use pre-configured loads or push packages to increase response time and decrease delivery time
Notes: Reference: FMI 4-90.1, pg. 6-89, para. 6-379 thru 8-388
Explaination of the 4th bullet: “(3-levels to worry about)”:
  1st level: ground level—driver eye-level
  2nd level: sky level—two, three, four story buildings offer cover and concealment for snipers, observers, etc.
  3rd level: sub-level—sewer systems, man-holes, underground facilities for enemy to move undetected.