## Slide 1: Maintenance Support
Maintenance Operations
& CL IX Distribution
For additional information or to help clarify information on a slide, select View and then drop down to select Notes Page.
Notes: FM 4-0, Combat Service Support, Chapter 8-1
Success on today’s battlefield demands that forces maintain, recover, repair, or replace equipment as quickly as possible. Good maintenance practices, forward positioning, of maintenance units, effective repair parts and equipment replacement systems, and clear priorities for recovery and repair are vital.
FM 4-30.3, Maintenance Operations and Procedures, para 1-41 – 1-43:
1-41. To maximize unit combat readiness, equipment must be repaired and returned to the user as quickly as possible. Repairs should be made as far forward as possible. Forward
means on-site or at the supported unit’s UMCP.
1-42. Recovery of equipment to maintenance collection points removes equipment from using units and increases the time it is not available. Repairing equipment as far forward as possible reduces transportation requirements and non-mission-capable time and increases equipment
availability.
1-43. Commanders must ensure the degree of maintenance performed is consistent with technical and tactical requirements. During combat, only maintenance needed to return equipment to mission-capable status is performed. This concentrates the maintenance effort on those areas that affect the outcome of the battle.

## Slide 2: TLO and ELOs
Terminal Learning Objective: Describe maintenance mission support capabilities and operational considerations for maintenance support
Enabling Learning Objectives:
A. Describe the mission, organization, capabilities, and operational considerations in employing maintenance units
B. Compare and contrast maintenance operations in support of diverse operations
C. Describe the responsibilities of maintenance management personnel and the STAMIS for managing maintenance support operations
D. Describe the methods to overcome maintenance and Class IX shortfalls
E. Describe Class IX repair parts request and distribution

## Slide 3: References
AR 750-1, Army Materiel Maintenance Policy, 15 Jul 2005
FM 3-04.500, Army Aviation Maintenance, 31 Mar 2005
FM 3-06.11, Combined Arms Operations in Urban Terrain, 28 Feb 2002
FM 3-07, Stability Operations and Support Operations, Feb 2003
FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, 15 Mar 2005
FMI 3-90.6, Heavy Brigade Combat Team, 15 Mar 2005
FM 4-0, Combat Service Support, Aug 2003
FM 4-30.3, Maintenance Operations and Procedures, Jul 2004
FMI 4-90.1, Heavy Brigade Combat Team Logistics, 15 Mar 2005
FM 4-93.2, The Sustainment Brigade, Cord Draft 14 Oct 2005
Notes: NOTE the acronym, FMI, used for Field Manual Intermediate. Each FMI published March 2005 has an expiration date of 15 March 2007.
Five FMIs were published 15 March 2005 in order to expedit delivery of doctrine urgently needed to execute transformation to modular brigade combat team organizations. FMIs address operations for HBCTs organized under the Army modular concept that governs the development of equipment, training, and restructure of former divisional brigades. Although the FMIs have not been through the standard doctrine development process, doctrine contained in them is authorized for implementation.
FMI 4-90.1 is the primary reference for logistics support of the modular HBCT.
To remain current with modular force doctrine, recommend that you link to the Center for Army Lessons Learned (CALL) website for Army Transformation (SBCT & Modular Force) at https://call2.army.mil/focus/transformation.

## Slide 4: Acronyms List
BCS3 Battle Command Sustainment Support System
BDAR Battle Damage Assessment and Repair
CABSA Combined Arms Battalion Support
Area
C&C Classification and Collection
FBCB2 Force XXI Battle Command Sustainment Support System
FSC Forward Suppot Company
MCO Maintenance Control Officer
MCP Maintenance Collection Point
MCS Maintenance Control Sergeant
OR Operational Ready
ORF Operational Readiness Float
PMCS Preventive Maintenance Checks and Services
SAMS-1E/2 Standard Army Maintenance System-1 Enhanced
SARSS1/2/2A Standard Army Retail Supply System
STAMIS Standard Army Management Information System
ULLS-G Unit Level Logistics System- Ground
UMCP Unit Maintenance Collection Point
Make http://www.acronymfinder.com a favorite search site to find the meaning of acronyms and abbreviations.
Notes: <number>
MAINTENANCE SUPPORT

## Slide 5: Outline
Maintenance Support Fundamentals
Modular Support Concepts
Maintenance Organizations (Missions and Capabilities)
Key Maintenance Managers
Employment on the Battlefield
  Maintenance Units
  Class IX Supply Distribution
Maintenance Support Planning Considerations
Sustaining and Managing Maintenance Readiness
Supporting Offensive, Defensive, Stability and Reconstruction, Civil Support, and Urban Warfare Operations
Notes: This lesson on maintenance support will follow the order listed on this slide.

## Slide 6: Maintenance Support Fundamentals
Maintenance entails actions taken to keep materiel in a serviceable, operational condition, restore it to a serviceable condition, or upgrade its functional utility through modification or product improvement
Maintenance support includes:
  Performing PMCS
  Recovering and evacuating disabled equipment
  Diagnosing equipment faults
  Substituting parts, components, and assemblies
  Exchanging serviceable materiel for unserviceable materiel
  Repairing equipment
Notes: ELO A FM 4-30.3, Maintenance Operations and Procedures, Page 1-1, para 1-1 & 8-18 – 8-23
8-18. PMCS are those maintenance tasks used to identify potential equipment problems. It includes quick turnaround repairs by component replacement, minor repairs, and performance of scheduled services at the operator, crew, company, and battalion/TF levels. PMCS also includes the performance of periodic scheduled checks to monitor the health condition of items of equipment.
8-19. Recovery is a critical battlefield capability that must be organic to all
tactical units and field maintenance activities. It includes the movement of
damaged, discarded, condemned, or abandoned allied or enemy materiel.
8-20. Diagnosing equipment faults allows the Soldier to identify malfunctions through the use of on-board sensors, external test equipment, and visual inspections.
8-21. Substituting. Removing serviceable parts, components, and assemblies fromunserviceable, economically reparable equipment, or from materiel authorized disposal, and immediately reuse it in restoring a similar item of equipment to a combat-operable or serviceable condition. Includes controlled exchange of parts and cannibalization.
8-22. Exchange. Issue serviceable materiel in direct exchange for unserviceable
materiel on an item-for-item basis.
8-23. Repair equipment. Field and sustainment maintenance activities will restore an item to serviceable condition through correction of a specific failure or unserviceable condition.

## Slide 7: Maintenance Principles
Replace Forward and Repair Rear
  Refers to replacing components or subcomponents at the point of repair, the breakdown site, or the unit maintenance collection point (UMCP)
  Uses distribution and evacuation channels to push components and end items to the sustainment level of repair
Anticipate Maintenance Requirements
  Maintenance leaders and managers must anticipate the requirements for support.
  Diagnostic data helps maintenance leaders anticipate future reliability of a component and provides maintenance managers the ability to preposition repair parts and maintenance personnel.
Notes: ELO A FM 4-0, Combat Service Support, Page 8-2 to 8-3
FM 4-30.3, Maintenance Operations and Procedures, Page 1-15, para 1-29--1-33:
1-29. The cornerstones of maintenance support are the tenets, “fix forward” and “anticipate support.” Repairing equipment far forward enhances the ability to quickly return the maximum number of combat systems, at the earliest opportunity, as close to the using unit as possible.
As maintenance operations transform with FXXI and beyond, maintenance concepts are evolving in replacing modular components forward and “fixing” in the rear.
1-30. Replace Forward and Repair Rear is the replacing of LRUs or modules instead of attempting to repair them. The LRUs or modules are retrograded to higher levels of
maintenance for repair and returned to the distribution system.
1-31. Replace Forward means a soldier performs “on-system” maintenance. “On-system” refers to replacing components or subcomponents at the point of repair, the breakdown site, or the UMCP.
1-32. Repair Rear means that soldiers perform “off-system” maintenance. “Off-system” refers to those actions taken to return components and subcomponents of weapon systems to serviceable condition. These repair actions take place at designated places throughout the battlefield.
1-33. Anticipating maintenance requirements allows prepositioning of maintenance support capabilities. Anticipation rests on the ability to foresee future operations and to identify, accumulate, and maintain the assets, capabilities, and information required to support them.
Anticipatory maintenance on the battlefield begins with the information obtained from the embedded diagnostic sensors located on the weapon system. The sensor will feed the maintenance and supply data to the on-board computer. This will be communicated to appropriate supporting activities so the requisite maintenance support will be available when and where required. When the Combat Repair Team (CRT) arrives at the repair site, they will use interactive electronic technical manual (IETM) compact disks, and test, measurement, and diagnostic equipment (TMDE) to confirm the sensor information and
ensure there are no additional failures.

## Slide 8: Maintenance Operations at Each Level of War
Strategic Level: Maintenance operations are largely conducted by depots throughout the continental United States (CONUS) based industrial and civilian sectors. Maintenance management at this level primarily links the nation’s economic base to its military operations in theaters.
Operational Level: Maintenance operations link strategic capabilities to tactical requirements. Managers coordinate direct support (DS) and general support (GS) maintenance, specialized/forward repair activities, and base logistics operations. The maintenance system both drives and supports the supply system.
Tactical Level: Maintenance operations consist of activities required to keep weapon systems operational during battle, supporting the tactical commander’s scheme of maneuver. Managers oversee operator/crew, unit, and DS maintenance operations. The primary focus is equipment repair or replacement and return to user.
Notes: <number>
MAINTENANCE SUPPORT
ELO A
FM 4-0, Combat Service Support, Pages 8-1 to 8-2, Chapter 8-1 to 8-7
FM 4-30.3, Maintenance Operations and Procedures, pg 1-4, para 1-12
Maintenance support includes maintenance activities at all levels of war. The slide provides a brief discussion of each level of war.
Strategic Support. The strategic base is the backbone of the national maintenance program and the sustainment maintenance system. At this level, maintenance supports the supply system by repairing or overhauling components or end items not available or too costly to procure. Maintenance management concentrates on identifying the needs of the Army supply system and developing programs to meet them. Strategic support also includes maintaining prepositioned equipment.
Operational Support. The goal of operational level is to support the operations plans and objectives of the commander. Its primary purpose is to provide field maintenance and to maximize the number of operational combat systems available to support the tactical battle.
Tactical Support. The nature of the modern battlefield demands that the maintenance system repair equipment quickly and at, or as near as possible to, the point of failure or damage. This requirement implies a forward thrust of maintenance into division and brigade areas where the battle is more violent and the damage is greater. Maintenance assets move as far forward as the tactical situation permits to repair inoperable and damaged equipment and return it to the battle as quickly as possible.

## Slide 9: Ground Maintenance Methods of Support
Forward Support
  Quick turn-around time to user
  Repair end items as far forward as possible (Fix Forward)
Area Support
  Defined geographic area
  Focus on units passing through or assigned to a specific area
Backup Support
  Designed for supported units with
  excessive maintenance requirements
  Provided by like maintenance units
Passback Support
  Evacuate maintenance requirements to a higher level of maintenance
Notes: <number>
MAINTENANCE SUPPORT
ELO A FM 4-30.3, Maintenance Operations and Procedures, page 1-16, para 1-35; Table 1-6
1-35. There are four methods of support used by maintenance organizations.. The fours methods are:
• Forward support. Maintenance-oriented toward quick turnaround to the user in order to maximize operational time by minimizing repair and evacuation downtime. End item repair thrust as far forward as possible within tactical time criteria, or recovered and evacuated to the point whererepairs can be made. “
• Area support. Maintenance resources concentrated in a defined geographic area based on the type and quantity of equipment supported. Focus is placed on the supporting units operating in or moving through defined geographic boundaries.
• Backup/Reinforcing support. Customer backup support is provided to the supported unit for excessive maintenance requirements that cannot be performed due to time or resource limitations. Backup support is provided to like-maintenance units for temporary excessive requirements that must be performed to meet operational readiness needs.
• Passback support. Passback support is provided by one maintenance unit to another supported maintenance unit. This requirement is a predictable and permanent maintenance workload that is allocated by force structure.
Photo shows a Forward Repair System placing an engine in a M1 Tank.

## Slide 10: Maintenance Operational Techniques
Battle Damage Assessment and Repair (BDAR)
Maintenance Collection Points (MCPs)
Recovery/Evacuation
Controlled Substitution/ Cannibalization
Notes: ELO A FMI-3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 10-23, Chapter 10-66
FM 4-30.3, Maintenance Operations and Procedures, para 1-38 & 1-39, 3-103; Chapter 6
Battle Damage Assessment and Repair (BDAR) is the procedure used to return disabled equipment to the battlefield by expediently fixing, bypassing, or jury-rigging components. It also includes the use of cannibalization of equipment. It restores the minimum essential combat capabilities necessary to support a specific combat mission or to enable the equipment to self recover. FM 4-30.3, para 3-101: BDAR actions include the following:
  • Using shortcuts to install or remove parts.
  • Modifying and installing components designed for other vehicles or equipment.
  • Using parts serving a non-critical function on a like vehicle.
  • Jury-rigging to bypass non-critical components.
  • Cannibalizing critical repair parts.
  • Fabricating critical parts.
3-103. Anyone on the battlefield can perform some BDAR. The operator/crew performs initial BDA and repairs the damage if possible. The commander decides whether or not to use BDAR instead of normal maintenance procedures. Since it may not be possible to train BDAR techniques in peacetime using actual equipment, the best substitute is to train system-oriented crews and mechanics to understand the theories and principles associated with weapon systems.
Recovery is performed by the owning unit. The owning unit is responsible for recovery of its equipment. Equipment should not have to be taken any farther to the rear than absolutely necessary. At no point should a vehicle have to be pulled by a M88 any farther than the UMCP. This practice keeps the brigade’s tracked assets forward and available for recovery missions.
Evacuation differs from recovery in that evacuations in conducted by another unit. Evacuation is the point at which maintenance and transportation meet. Evacuation is a supplementary transportation mission normally handled by the MSB’s TMT company or the heavy transportation companies. The Support Operations Officer has the mission to coordinate with the MCO or the nearest Movement Control Team (MCT).
Controlled Substitution is the replacement of a serviceable part on one vehicle with an unserviceable part from a second vehicle in order to get the second vehicle fully mission capable. The key point is that the part is replaced on both vehicles. Additionally, the part is ordered and records are maintained, so that when the part comes in, it goes towards that particular job.
Cannibalization is the authorized removal of a part with no intention of replacing it. Peace-time cannibalization occurs at “bone-yards” established by the DOL or major subordinate command.

## Slide 11: Two-Level Ground Maintenance Concept
Field Maintenance-- Repair and return end items for immediate use by the supported unit
  -- Unit Maintenance -- Direct Support (DS) Maintenace
Sustainment Maintenance-- Repair major end items and return them to the supply system
  -- GS Maintenance -- Depot Maintenance
Characteristics of the two-level maintenance system:
Eliminates maintenance echeloning
Returns equipment to the fight faster
Reduces the logistics footprint in the battlespace
Reduces repair cycle time to sustain combat power
Incorporates the tenets of battlefield distribution
Notes: <number>
MAINTENANCE SUPPORT
ELO A
FM 4-0, Combat Service Support, Page 8-5, Chapter 8-19
FM 4-30.3, Maintenance Operations and Procedures, Page 1-14, para 1-35 – 1-27, Chapter 8
AR 750-1, Army Materiel Maintenance Policy, Chapter 3-8 to 3-9
Maintenance levels form the baseline for determining which specific maintenance tasks are assigned to each level. They are a means to select the scope of maintenance and the skill levels necessary for unitsand activities at various command levels.
The modular organizations continue to build on the two-level maintenance system, comprised of field maintenance and sustainment maintenance. The two-level maintenance system is one that essentially combines the AOE unit and DS levels of maintenance (called “field maintenance”) and the AOE GS and depot levels (called “sustainment maintenance”).
Field maintenance involves on-system tasks normally done by assets internal to the organizations that return systems to a mission capable status. Field maintenance is
repair and return to user. At field maintenance level all functions are focused on replace and return to the user. The overarching goal is to reduce repair cycle times by providing capabilities as far forward on the battlefield as possible, maximizing reliance on parts distribution, visibility, and replacement.
Sustainment maintenance is repair and return to supply. It is generally performed above the DSlevel. It involves off-system tasks that are done primarily in support of the supply system (repair and return to supply). It will not normally be performed inside the brigade battle space. This level of maintenance is focused on repairing components, assemblies, modules, and end items in support of the distribution system. The intent of this level is to perform commodity-oriented repairs on all supported items to one standard that provides a consistent and measurable level of reliability.

## Slide 12: Two Levels of Aviation Maintenance
Field Maintenance
  Flight companies/flight troops and aviation maintenance
  companies/aviation maintenance troops
    Perform authorized unit maintenance
    Perform high frequency "on aircraft" maintenance tasks.
  Aviation support company within an aviation support battalion (ASB)
    Repair materiel for return to user
    Replacement and repair of modules and components
    Furnish quick response maintenance support and technical assistance through the use of mobile maintenance support teams and aircraft recovery and evacuation
Sustainment Maintenance
  Theater aviation sustainment maintenance groups, depots, the original equipment manufacturers’ maintenance and overhaul facilities
    Aircraft recapitalization and overhaul
    Crash and battle damage repair
    Major airframe modifications.
Notes: <number>
MAINTENANCE SUPPORT
ELO A AR 750-1, Chapters 6-4 and 6-6, pages 66-67
During the early stages of a conflict, heavy requirements are placed on all aviation assets. Aircraft readiness, and the ability to support that readiness, must be assured. This requires extensive use of aviation maintenance companies/aviation maintenance troops providing forward support at the field maintenance site where the major thrust is remove-and-replace maintenance. An adequate available stock of components and the capability to repair them at the aviation support company, ASB is essential.
As the battle continues, extensive aircraft maintenance, whether done by aviation maintenance companies or an aviation support company, will be performed in the division rear area.
An aggressive controlled exchange policy, the rapid recovery of damaged aircraft, and a flexible system of cross-leveling spares will be required. Implicit in the remove-and-replace maintenance approach is the deferment of phased maintenance tasks not related to safety-of-flight and an almost total shift to on-condition maintenance during actual combat operations or emergencies.
NOTE: AOE aviation maintenance force structure provided three levels of aviation maintenance:
  Aviation Unit Maintenance (AVUM)
  Aviation Intermediate Maintenance (AVIM)
  Depot Maintenance
AR 750-1, published 15 Jul 05, changed aviation maintenance to the same two level maintenance followed by ground maintenance forces: field maintenance and sustainment maintenance.

## Slide 13: Overview of Key Units and Tasks
CO LVL FMT
PLT HQ
MNT CNTRL SEC
RCVRY SEC
BASE MAINT
SEC
FIELD MAINT PLT
Systems Used
SAMS-1E
Key Tasks
BCT Field Maintenance
Reinforcing support to FSC
Systems Used
SAMS-1E
Key Tasks
Battalion/Squadron Field Maintenance
Key Tasks
Division/Corps Field Maintenance
Key Tasks
Repair and return components to the supply system
FIELD MAINT CO
PLT
HQ
REC
SEC
MECH
MAINT
SEC
PLT
HQ
ELEC/
MSL SEC
GSE SEC
ARMT
SEC
CO
HQ
MNT CNTRL SEC
AREA SPT PLT
BASE SPT PLT
Details on following slides
BSB
FSC
Division/Corps
CSSB
Notes: ELO A
Generally speaking, all DS and unit maintenance functions (field maintenance) are consolidated in the FSCs and BSB maintenance activities. This applies to all maneuver and supporting brigades. This design allows each level to focus support on its own organization

## Slide 14: Maintenance Organizations
HBCT
  Forward Support Company’s Field Maintenance Platoon
  BSB’s Field Maintenance Company
Division [Sustainment BDE’s Maintenance Organization]
  Support Maintenance Company
Corps [Sustainment BDE’s Maintenance Organization]
  Support Maintenance Company
  Component Repair Company
  Collection and Classification Company (C&C)
Notes: ELO A
The employment, mission, organization, and capabilities of this maintenance organization will be described in subsequent slides.

## Slide 15: Employment – BDE Level
BSA
BDE (-) ALOC
BDE
S-1
BDE
S-4
BSB
SPO
BSB
DC
FMC
MED
MP
MI
BSB
Mission: The FMT from the FSC provides dedicated automotive, track field maintenance, and recovery capability to the maneuver/combat companies.
Mission: The BSB provides field maint and supply to the BDE. The FMC provides field maint to units of the BDE not supported by an FSC. It is strictly reliant on Line Replaceable Units (LRUs), combat spares, and floats to conduct MNT operations.
Mission: The FSC provides field maint and supply to its supported BN/TFs. The S&T platoon provides parts distribution. The maintenance platoon can function consolidated or split based, depending on METT-TC.
FSC
FMT
(-)
(-)
(-)
(-)
FMT
II
II
Combat Trains
FSC
UMCP
FWD (-)
BAS
TF S-1/S-4 (-) SPT OP
(CTCP)
CABSA
FSC
FSC CDR/1SG
(-)
TF S-1/S-4 (-)
CO Supply SGTs
(LOGPACS)
FMT
FMT
FMT
LRP
BN HQ/FSC
(-)
Combat Trains
FSC
UMCP
FWD (-)
BAS
TF S-1/S-4 (-) SPT OP
(CTCP)
FA BN
FSC
FSC CDR/1SG
(-)
TF S-1/S-4 (-)
CO Supply SGTs
(LOGPACS)
FMT
LRP
FMT
Combat Trains
FSC
UMCP
FWD (-)
BAS
TF S-1/S-4 (-) SPT OP
(CTCP)
CABSA
FSC
FSC CDR/1SG
(-)
TF S-1/S-4 (-)
CO Supply SGTs
(LOGPACS)
II
II
FMT
FMT
FMT
FMT
LRP
= Supported by BSB
= Primary Supply route
= Alternate supply route
(-)
FSC/BN HQ
FSC provides Field Maint and supply support to the Brigade Recon Troops based on METT-TC
FMT
FMT
FMT
LRP
Notes: ELO A FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 10-2, Figure 10-1; Page 10-7, Figure 10-2
This chart provides an overview of employment of maintenance support organizations at the BDE level.
Each level in the brigade has the capability to support it’s own modular organization. Current designs allow for battalion organizations with embedded FSCs. If you significantly change the number of companies within the battalion, you will change the required support for the FSC.
The goal of the design is to allow each level to focus support on its own organization. As a result, the FSC aligned to a battalion focuses support on its battalion. The BSB in the brigade focuses support on its brigade.
This concept maximizes unit distribution as far forward on the battlefield as possible.
METT-TC and intensity of operations demand flexibility in the positioning and stationing of logistics assets.

## Slide 16: HBCT’s Maintenance Support Organization
BTB
BSB
DISTRO
CO
FLD MNT
CO
HHC
MED
CO
FSC
DISTR
PLT
HQ
FLD MAINT
PLT
FSC
DISTR
PLT
HQ
FLD MAINT
PLT
FSC
DISTR
PLT
HQ
X
BDE
ATHP
SEC
FLD MAINT
PLT
This diagram depicts the current modular design for a Heavy Brigade Combat Team. This design is used for all fixed BDEs comprised of battalions with FSC structures
Notes: ELO A FMI 3-90.6, Heavy Brigade Combat Team, Page xxv, Figure Intro-8; Page 2-9, Figure 2-8 FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 2-1, Chapter 2-1
The goal of the HBCT’s modular design is to develop a brigade that is independent and not tied to other organizations or structures for support. Critical decisions were made to embed support at the lowest level.
Brigade Support Battalion (BSB). The BSB provides field maintenance and supply to the BDE. The FMC provides field maint to units of the BDE not supported by an FSC. It is strictly reliant on Line Replaceable Units (LRUs), combat spares, and floats to conduct MNT operations.
Forward Support Company (FSC). Each maneuver BN or BN designed with FSCs has its own organic support accomplished through the FSC. The FSC is responsible for all logistics support to the supported battalion. Automotive and track vehicle repair functions are accomplished by FMTs. This design is not new; it expands the design started in FXXI by carrying it to the artillery battalion in addition to the RSTA.
With this design, each battalion is capable of conducting it’s own maintenance support without reliance on another organization to conduct certain maintenance functions.

## Slide 17: BSB Field Maintenance Company
Mission: Provide field maintenance to the BCT, BDE HQ, and BSB; area support to units within the BSA; and reinforcing support to the FSCs.
Functions:
Provide recovery, Auto/Armt, Ground Support, and Electronics maintenance and maintenance management to the Brigade Base Elements (HQ, BSB, BTB).
Provide maintenance advice and support to the brigade.
Serve as the central entry and exit point to the BDE for low density equipment.
FIELD MAINT CO
CO
HQ
PLT HQ
MAINT PLT
MAINT CNTRL SEC
PLT HQ
PLT
HQ
MECH MAINT SEC
GSE REPAIRSEC
SVC & RECOV
BSB
Notes: ELO A
FMI 3-90.6, Heavy Brigade Combat Team, Page 10-24, Chapter 10-65 to 10-67
FMI 4-90.1, Heavy Brigade Combat Team Logistics, Page 5-162
The maintenance company is responsible for conducting maintenance for the HQ, BTB and itself (the BSB).

## Slide 18: FSC Field Maintenance Platoon (Combined Arms Battalion FSC)
Mission: Provide field level maintenance to the battalion/squadron
Functions: Provide recovery, Auto/Armt, Ground Spt, and Electronic/MSL maintenance and maintenance management to the battalion base elements (HQ, FSC) and company level Field Maintenance Teams (FMTs).
FMT
(EN)
0-0-11 (x1)
FMT
(AR)
0-0-9 (x2)
Maint
2-1-138
Plt HQ
1-0-1
Maint Ctl
Section
1-1-6
Recovery
Section
0-0-14
MNT
SVC
0-0-62
FMT
(MECH)
0-0-13 (x2)
HQS
2-0-5
Dist
1-0-60
Maint
2-1-138
FSC
5-1-228
Notes: ELO A FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 10-5 and Page 10-9, Chapter 10-22
CAPABILITIES: FMTs to company level for automotive/tracked vehicle maintenance support. Base Field Maintenance Section for area support (BN HQ and FSC) in addition to limited low density equipment (ELEC, MSL, GSE, and ARMT) support to the FMTs. Allows attachment of company level assets to other BNs for limited durations. Maximizes LRUs replacement, Combat Spares (PLL, Bench/Shop Stock) and BDAR. Maintenance management functions performed by SAMS-1 and ULLS-G.
The FSC Field Maintenance Platoon (FMP) base section consolidates low density equipment repair (generator, AC, CHEM QM, and electronic/missile) for the entire battalion. Based on the availability of critical test equipment, the electronic functions may need to be consolidated at the BSB Field Maintenance Company (FMC) Electronic Section in the near term.
BDE designs with low equipment densities (for example the Infantry BDE) may consolidate automotive and track functions at the base section to allow for a more economic pooling of assets that can be dispatched and tailored for support based on METT-TC

## Slide 19: Field Maintenance Teams
Mission: Provide field maintenance (unit and DS maintenance) for all combat platforms organic to maneuver companies
Maneuver Company Commander sets priorities
FMT operates under the control of the Company 1SG
The FMTs perform repairs as far forward as possible, returning the piece of equipment to the battle
  Carry limited on-board combat spares to help facilitate repairs forward
Major Equipment:
  M113 Personnel Carrier
  M88A2 Recovery Vehicle
  5-ton Cargo Truck
  Contact Maintenance Truck
  Forward Repair System
Notes: ELO A FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 10-10, Chapter 10-27; Page 10-12, Chapter 10-38 to 10-39
FMI 4-90.1, Heavy Brigade Combat Team Logistics, Page 3-64, Chapter 3-247
During combat, FMTs will perform BDAR, diagnostics, and on-system replacement of line replaceable units (LRUs). Emphasis is placed on troubleshooting, diagnosing malfunctions, and fixing the equipment by component replacement.
If the tactical situation permits, FMTs focus on completing jobs on site.
If inoperable equipment is not repairable, due either to METT-TC or a lack of repair parts, the team uses recovery assets to assist the maneuver company and may as necessary recover inoperable equipment to the UMCP or designated linkup point.
Habitually associated FMTs with the associated ULLS-G boxes move with a supported unit in order to maintain support to the company. The ULLS-G box and the operator will normally stay in the UMCP.
Organizational and DS work orders are tracked by the MCS. The MCS gives the FMT a block of work order numbers to track equipment repair. The FMT NCOIC uses the free text message on the CFS via FBCB2 to update the MCS on work order status.

## Slide 20
Mission: The sustainment brigade plans, prepares, executes, and assesses combat service support operations within an assigned AO
CSSB
CSSB
CSSB
CSSB
CSSB
CSSB
SUS
BTB
HHC
SIG
CSSB
FIN
HR
AMMO
TRANS
MAINT
S&S
HHC
MFMB
OPCON
Modular Sustainment Bde
Notes: FMI 3.90.6, Page XXXI ELO A
As a result of two level maintenance, component repair functions were migrated out of the BDEs and placed in the Sustainment BDE.

## Slide 21: Support Maintenance Company
Conduct DIV/Corps area field maintenance support.
Support theater opening packages
Capability to accept modules (platoons/sections/teams) from Component Repair Companies (CRC) and Collection and Classification Companies (C&C)
SMC
GSE Plt
43573FG
Track Mnt
Mod
43573FC
Wheel Mnt
Mod
43573FD
SP Fld Arty
Mnt Mod
43573FE
MLRS
43573F0
ADA
43573FR
Missile Plt
43573FM
43573FM
Track Rec
Mod
43573EO
Elec
Plt
43573FJ
Auto/Armt
43573FB
SMC
43573
Serv/Rec
Sec
Mnt
Cntrl
Sec
HQs
43473FA
LCMS
43573FN
15
2
2
34
27
43
24
27
8
9
Approx. 200-250 soldiers (Capable of supporting up to
20 contractors) METT-TC dependant
HIMARS
43573FR
18
RDR/GBS
Maint Mod
43573FI
COMMEL
Maint Mod
43573FJ
GSE Mod
4357FH
Towed
Arty Mod
43573FF
11
9
3
4
9
Notes: ELO A
FM 4-30.3, Maintenance Operations and Procedures, page 8-6, Chapter 8-13.
MISSION: To command and control assigned cellular platoons, modules, and teams performing field maintenance (on-system repair and replacement) return to user operations.
FUNCTIONS: Provides command, control, administrative, and logistics support for combinations of assigned platoons, modules, and teams performing field maintenance. This company and its assigned platoons, modules, and teams employ at echelons above the BCT based on required workload. All modules start with platoons and add team modules based on additional workload above the platoon level. Tracked Vehicle Recovery Teams may be assigned when tracked vehicle recovery operations are required
CAPABILITIES: Command, control, and supervision of subordinate elements performing field maintenance functions.
Span of control of the company headquarters element normally will not exceed 250 personnel. Unit can integrate civilian augmentation from the Logistics Support Element (LSE) as required. Civilian augmentation personnel may comprise approximately 10 percent of the overall unit strength.
Provide Mission Staging Operations (MSO).

## Slide 22: Component Repair Company
Provide repair and return to the supply system (sustainment maintenance support)
Operate in conjunction with a supply support activity (SSA)
Can receive attachment of augmentation modules based on workload and tactical situation
Integrate maintenance repair activities with AMC
CRC
GSE Rep
Plt
43583FC
Auto/Elec
Rep Plt
43583FF
DESETS
Aug TM
43583FH
BSTF Aug TM
43583FK
GVLLD
Spt Tm
43583F100
NSTF
Spt Tm
43583FJ00
Comp Rep
Plt
43583FG
Elec Rep
Plt
43583FE
Armt Rep
Plt
43583FD
Auto Rep
Plt
43583FB
CRC
43583
Serv/Rec
Sec
Mnt
Cntrl
Sec
HQs
43483FA
TMDE
Spt
Tm
43547AH00
7
7
59
23
26
35
61
5
15
2
6
4
Approx. 140-160 soldiers
(METT-C)
Field maintenance functions previously consolidated at the division MSB
Notes: ELO A FM 4-30.3, Maintenance Operations and Procedures, page 8-7, para 8-15:
8-15. Component Repair Companies (CRCs) will replace existing GS maintenance units. The principle difference between CRC and GS maintenance companies is the new unit only focus is the repair of components. CRCs, unlike GS maintenance units, may be located outside the AO; at any point in the distribution pipeline to repair retrograded material moving through the supply system. The CRC will not provide
area recovery support or send out FMTs.
MISSION: To command and control assigned cellular platoons, modules, and teams performing sustainment maintenance operations (off-system repair and return to the supply system).
FUNCTIONS: Provides command and control; administrative and logistics support for combinations of assigned platoons, modules, and teams performing sustainment maintenance. Tailored to meet operational mission requirements. All modules start with platoons and add team mods based on additional workload above the platoon level. May be assigned at any location in the distribution system.
CAPABILITIES: Command, control, and supervision of subordinate platoons performing sustainment maintenance functions.
Span of control of the company headquarters element will not exceed 176 personnel.
Unit can integrate augmentation civilian personnel and equipment from the Logistics Support Element (LSE) as required. Civilian augmentation personnel comprises approximately 10 percent of the overall unit strength.
.

## Slide 23: Collection and Classification Company (C&C)
l
COLLECTION & CLASSIFCATION COMPANY
STORAGE & SHIPPING PLATOON
DISASSEMBLY PLATOON
MAINTENANCE CONTROL PLATOON HQ
COMPANY HQ
DET HQ
2 DISTRIB
HUB TEAMS
0-0-12
..
12
158
1-0-19
20
DISASSEMBLY PLATOON HQ
2
1-0-1
..
EQUIMENT DISASSEMBLY SECTION
41
0-1-40
..
11
IDENT & INSPECTION SECTION
0-1-10
..
..
ARMAMENT DISASSEMBLY SECTION
11
0-1-10
..
PACKING & CRATING SECTION
0-0-5
5
..
DET HQ
6 WPN SYS RECOVERY TMS
18
0-0-18
..
2
FORWARD COLLECTION PLATOON HQ
1-0-1
..
MAINTENANCE CONTROL & PLATOON HQ
1-0-3
4
..
HEAVY LIFT & EVAC SECTION
13
0-0-13
..
..
TEMP STOR & SHIPPING SECTION
17
0-0-17
STORAGE & SHIPPING PLATOON HQ
1-0-1
2
..
15
54
24
FORWARD COLLECTION PLATOON
32
MISSION: Establish and operate a C&C facility for the receipt, inspection, segregation, disassembly, preservation, and disposition of serviceable and unserviceable Class VII and IX materiel and similar foreign materiel
Notes: <number>
MAINTENANCE SUPPORT
A limited number of Collection and Classification companies remain in the force structure to provide for the the execution of cannibalization points and the disposition of Class VII items and their components. This unit will operate at the rear area of the AOR normally associated with what was the theater rear.
Mission limitations: except items peculiar to cryptographic materiel, missile systems, aircraft, airdrop equipment, drones, and medical materiel
CAPABILITIES: -Performs disassembly of end items that have been declared economically repairable and classification of components and assemblies for repair, return to supply stocks, or disposal. -Segregates, preserves, and packages selected items of materiel and related components for return to supply channels for evacuation and technical intelligence evaluation. -Operates a cannibalization point, when authorized by higher headquarters. -Distribution Hub Teams perform vital maintenance inspection functions at distribution hubs along the distribution pipeline. -Return serviceable Class VII and IX materiel at the direction of the MMC.

## Slide 24: Key Maintenance Managers
FSC Maintenance Control Officer
BSB SPO Maintenance Cell
Sustainment Brigade SPO/ Distribution Management Center (DMC)
  Distribution Division
    Maintenance Branch
      Automotive-Ground Support Equipment Branch
      Electronics-Calibrations Branch
      Missile Branch
Notes: ELO C
Maintenance management in the HBCT will require close coordination and collaboration between the Battalion/Brigade S4s, the support operations staff, CRTs, and the MCO.
For tthis lesson, you will focus on maintenance management at BSB SPO and below. It is similar to AOE, managed through the sustainment brigade.
For the break down for the SPO/DMC maintenance branch, refer to the CSS Overview lesson slide.

## Slide 25: FSB Maintenance Control Officer (MCO)
The MCO is the senior maintenance officer in the FSC providing field maintenance to his supported battalion. He additionally serves as maintenance officer for that battalion.
MCO Responsibilities:
Evaluate and ensure the quality of maintenance completed by the maintenance platoon
Coordinate for the recovery of battalion equipment
Monitor the status of equipment under-going repairs and determine Class IX repair parts status
Plan for continuity of maintenance support
Manage production control, to include the assignment of work to shop sections and the compilation of prescribed reports and records
Notes: ELO C FMI 4-90.1, Heavy Brigade Combat Team Logistics, Page 3-62, Chapter 3-240
NOTE: Maintenance Control Officer equals Shop Officer.
3-240. The maintenance control officer is the principal assistant to the commander, both
battalion and FSC, on all matters pertaining to the field maintenance mission. The MCO
serves as maintenance officer for the maneuver battalion. He is also is the senior person in the UMCP and is responsible for the local security requirements and tying in with adjacent units. He is responsible to the commander for the management of the combined efforts of the maintenance control section, maintenance section and service and recovery section, and the maintenance system teams to include those listed on this slide and the following slide.
􀁺

## Slide 26: FSB Maintenance Control Officer (MCO)
Coordinate the activities of the inspectors and maintenance personnel to ensure adherence to the maintenance standard
Execute maintenance priorities as established by the maneuver battalion commander
Anticipate expected workloads, shop progress, difficulties encountered during repair actions
Coordinate field maintenance requirements with maneuver battalion S-4 and BSB SPT OPNS as appropriate
Develop the maintenance services plan for battalion equipment
Integrate BSB and sustainment brigade maintenance teams into the FSC
MCO Responsibilities (continued):
Notes: ELO C
FMI 4-90.1, Heavy Brigade Combat Team Logistics, Page 3-62, Chapter 3-240

## Slide 27: Maintenance Cell, BSB SPO
Maint Cell
Sup & Svc Cell
Trans Mgt Cell
HSS Cell
Ammo Cell
Contract Cell
SPO
Develop the plans and policies for reparable exchange and Class IX operations
Monitor shop production and job status reports in the Field Maintenance Company and FSCs
Monitor and review the combat spares and coordinate critical parts status with the sustainment brigade
Review backlogs on critical weapon systems with the Brigade S4
Notes: ELO C
FMI 4-90.1, Heavy Brigade Combat Team Logistics, Page 3-16, Chapter 3-55-3-57
3-57. The support operations maintenance cell develops the plans and policies for reparable exchange and Class IX operations. It monitors shop production and job status reports in the field maintenance company and FSCs. It also monitors and reviews the combat spares and coordinates critical parts status with the sustainment brigade. For unserviceable items, the SAARS box in the distribution company generates disposition instructions based on brigade commander’s guidance. Instructions include evacuation, cannibalization, and controlled exchange policies. With the brigade S4, it reviews backlogs on critical weapon systems. For any additional support requirements, the BSB support operations coordinates through the division sustainment brigade materiel management branch.

## Slide 28: Support Operations Maintenance Officer
SPO Maintenance Officer Responsibilities:
Monitor maintenance posture using SAMS-2
Forecast and monitor the workload for all equipment by type
Coordinate maintenance priorities with the Brigade S4
Coordinate Field Maintenance Company’s operations
Provide recommendations to the BCT S4 to redistribute FSC maintenance assets within the BCT
Track and investigate Class IX high priority requisitions
Assist with planning and coordinating contingency support
Coordinate maintenance back-up support with the sustainment brigade
Notes: ELO C
FMI 4-90.1, Heavy Brigade Combat Team Logistics, Page 3-11, Chapter 3-43
FM 4-90.1, para 3-57: The duties of the maintenance officer also include the following:
􀁺 Conducts continuous logistics preparation of the battlefield.
􀁺 Tracks and investigates Class IX high priority requisitions.
􀁺 Assists with planning and coordinating contingency support.
􀁺 Directs redistribution of maintenance workloads by BSB.
􀁺 Coordinates maintenance back-up support with the sustainment brigade.
􀁺 Monitors units’ maintenance posture using SAMS-2.
􀁺 Coordinates maintenance priorities with the brigade S4.
􀂄 Provides recommendations to the HBCT S4 to redistribute FSC maintenance
assets within the HBCT.
􀁺 Establishes maintenance priorities for workload management through coordination
with the supported unit.

## Slide 29: SUS BDE SPO Readiness Division & Maintenance Branches
SPO Readiness Division manages maintenance for the supported units. It provides integrated, automated maintenance management. This office plans and forecasts maintenance and related material requirements based on future operational plans.
Subordinate maintenance branches include the:
  Electronics Maintenance & Calibrations Branch
  Missile Branch
  Automotive-Graound Support Equipment Branch
  Aviation Maintenance Readiness Branch
Notes: ELO C FM 4-93.2 para 6-27-6-31
6-27. The readiness division manages maintenance for the supported units. It provides integrated, automated maintenance management for armament combat vehicles, automotive ground support equipment, communications electronics equipment and missile equipment. This office plans and forecasts maintenance and related material requirements based on future operational plans and it coordinates the disposal of enemy equipment. It supervises the preparation and maintenance of inventory and activity reports, and recommends cross leveling and evacuation of the maintenance workload. It prepares all maintenance plans and annexes for support plans and orders and provides status reports.
Electronics Maintenance and Calibration Branch
6-28. This branch performs integrated materiel management of communications equipment, communications electronics intelligence equipment, electronic warfare, combat surveillance, target acquisition and night vision equipment.
Missile Branch
6-29. The missile branch performs integrated materiel management for land combat and air defense missile systems to include classification and diagnosis of malfunctions, repair and replacement of parts, component overhaul, and testing and final inspection of equipment.
Automotive-Ground Support Equipment Branch
6-30. This branch performs the integrated materiel management for automotive and ground support equipment, including tactical wheeled and general purpose vehicles, construction and MHE, and test equipment for assigned material.
Aviation Maintenance Readiness Branch
6-31. The aviation maintenance readiness branch coordinates aviation and aircraft maintenance operations for customer units, manages equipment availability and readiness for all aircraft and aviation related systems, facilitates and expedites the turnaround time for repair and return of critical combat equipment, tracks monitors and determines trends and recommends solutions to aviation repair/parts issues.

## Slide 30: Class IX Supply Distribution Management
Sustainment
Base
Corps
Division
SUST
X
I
FSC
BSB
II
XX
TSC
II
SUST
X
I
FMT
I
CRC
I
CRC
Modularity Support Concept
- Modular Units / Capability
- Throughput Class IX to BSB
Mobile Storage of Combat Spares in the Field Maintenance Teams
Supports replace forward/fix rear
I
I
SAMS1-E
SARRS1
Sustainment BDE SPO
CSSB SPO
Sustainment BDE SPO
CSSB SPO
BN XO
BN S4
SARSS2A
SARRS1
SARSS2
Notes: ELO E
FMI 3-90.6, Heavy Brigade Combat Team, Page 10-23, Figure 10-7
FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 10-19, Chapter 10-61
Repair parts make up 92 percent of the total Army inventory.
The primary methods of returning systems to a mission-capable status are through the
use of Class IX repair parts, BDAR, controlled substitution, cannibalization, and Class VII replacement.
A unit’s PLL depends on its equipment, but parts should be limited to only those items preventing equipment from performing if the items failed. Small items with high-usage rates should be held as far forward as practical.
Requests for Class IX resupply will originate at a maintenance node (FMT or base shop) and travel through maintenance STAMIS’ to the supporting Class IX activity. Requests may also be sent via the FBCB2 or voice communication as an alternative. The mechanic
will determine the fault and input it into the IETM that will then order the necessary part(s) through the STAMIS.

## Slide 31: CL IX Requirements Flow
<date/time>
<footer>
= DATA FLOW
STAMIS Concept BCS3 at all logistics nodes for ITV/TAV
ULLS-G and SAMS-1 at the FSC
(SAMS-1E will integrate SAMS-1 and ULLS-G functionality)
SARSS-1 at the BSB Distro Co and Sust Bde QM Co
SARSS CTASC at TSC level (SARSS-2AD eliminated from the architecture)
CTASC Flyaway computers at BCT and Sust Bde SPOs for document research, error correction balance queries....
BSB
DIST
XX
DIV
X
BCT
QSC
BTB
FDP
FDP
DMC
CSSB
XX
TSC
DCP
SARSS-1
SARSS-1
SARSS/ CTASC
CTASC FLYAWAY
CTASC FLYAWAY
BCS3
BCS3
XX
SUST
BCS3
BCS3
XXX
Corps
OCP
CTASC FLYAWAY
BCS3
FSC
MNVR
CO
MNVR
CO
MNVR
BN
MNVR
CO
MNVR
CO
MNVR
CO
BCS3
SAMS-1
TRANSCOM
AMC/DLA
HSOC
FACTORY
Notes: ELO E
Repair parts support begins with a SARSS-1 Class IX requirement from the supported FSC Field Maintenance Team (FMT) that provides field maintenance support to maneuver units. If the requested Class IX item is contained in the unit’s combat load, it will be provided from the FSC Maintenance Platoon to the FMTs during CRO operations. The FSC will then be replenished with this item from the BSB Distribution Company during SRO operations.
If the item is not available in the unit’s combat loads, requests are forwarded to the Quartermaster Support Company in the Sustainment Brigade. If the Supply Company, CSSB in the division has the item, it is released and provided to the BSB during MSO operations.
If the part was not available, the request is forwarded to the Supply Company, CSSB, Sustainment Brigade for fill at the operational level.
If the item is not available at the division, corps, FOB, or ISB, the request will be sent to the strategic level.

## Slide 32: CL IX Distribution Flow
Corps
OCP
DIV
SUST
X
BCT
I
FSC
BTB
II
BSB
II
I
FSC
I
FSC
I
FSC
XX
TSC DCP
II
II
II
II
QSC
I
SUST
X
QSC
I
HUB
HUB
SARSS-1
SARSS-1
SARSS-1
TRANSCOM
AMC/DLA
HSOC
FACTORY
STAMIS Concept BCS3 at all logistics nodes for ITV/TAV
Mat’l Shipped to and accounted for in SARSS-1 at Sust Bde QM Co or BSB Distro Co
Policy is primarily “Pure pack” to ordering SARSS-1
Mat’l transported from BSB to FSC for issue to individual customers (or direct to customers where no FSC)
Class IIIP and IX go to ULLS-G and SAMS-1 at the FSC
PB items posted to PBUSE (Prop Book) before being issued. Hand receipts maintained on PBUSE at Co level
= Materiel Distribution
SARSS/ CTASC
Notes: ELO E
As with general supplies Class II, IIIP, IV, and VII, Class IX repair parts are stocked in the Supply Company, CSSBs at the Forward Distribution Points (FDP) at either the division or corps (or ISB, FOB), as appropriate.
The Supply Company, CSSBs will be co-located with the Component Repair Companies (CRC) and Support Maintenance Companies (SMCs) at both the division and corps FDPs.
Class IX items will be contained within the brigade’s three combat loads.
The Supply Company, CSSB has modular Area Support Platoons that will configure Class IX items or modules into configured loads for forward distribution. When feasible, Class IX items coming from the strategic level will be configured for throughput as far forward as the BSB. Due to its limited size, the FMTs will often require a daily resupply of mission-critical repair parts.
The Support Operations Supply and Services cell monitors, coordinates, and manages daily Class IX distribution to the FMTs. The Support Operations Maintenance cell develops the plans and policies for RX operations. It monitors shop production and job status reports in the FMC.

## Slide 33: Managing Battlefield Maintenance
Compute the unit’s needs
Parts required
Battle Damage Assessment
Command
Personnel
Publications
Time
Facilities
Test Equipment
Tools
Parts
Skills
Maintenance Support Forward
Commander’s guidance
BDAR
Controlled Exchange
Cannibalization
Recovery
Evacuation
Identify Requirements
Identify Available Resources
Manage for Maximum Return
Maintenance Resources On-Hand
Resources
Committed
Resources
Available
-
=
Notes: <number>
MAINTENANCE SUPPORT
ELO D
FM 4-30.3, Maintenance Operations and Procedures, Page 1-17, Figure 1-3
When requirements have been identified, the maintenance manager must identify the resources on hand versus those already committed. Available resources are then managed within the established support framework to return the maximum number of items to fully mission-capable status.
When a shift or change in priorities could provide a greater overall return, the maintenance manager takes appropriate action or makes recommendations through the chain of command.
Although the maintenance manager may not formally lay out a management matrix, as shown on this slide, a mental estimate of these factors is necessary.

## Slide 34: Measuring Maintenance Performance
Fleet FMC rates
Customer OR rates
Size and age of the backlog
Turn around time
  Maintenance delay time
  Supply delay time
  Repair cycle time
Backup support utilization
Operational readiness float (ORF) utilization rate
ORF transaction time
Repaired item rejection rates
Notes: <number>
MAINTENANCE SUPPORT
ELO C FM 4-30.3, Maintenance Operations and Procedures, Chapter 4
Turn around time (TAT) is the overall measure of the duration of the maintenance cycle. It gives an indication of the responsiveness of the maintenance organization to its customers. It covers the period of time from acceptance of a work order to closeout but does not include time awaiting customer pickup.
Although there may be variations among work orders, TAT can comprised three major components—maintenance delay time, supply delay time, and repair cycle time.
  Maintenance delay time is the component of TAT that represents time spent awaiting a required resource other than repair parts—that is, the availability of facility space, tools, TMDE, and skilled personnel. It also includes time awaiting initial, in-process, and final inspections and time awaiting induction into the shop.
  Supply delay time is the component of TAT that represents time lost waiting for receipt of repair parts. It includes only that time when no further maintenance action can be taken because of a lack of repair parts. Time elapsed while repair parts are on order but other maintenance actions are, or could be, taken will not be counted as supply delay time.
Backup support utilization is a measure of the extent of workload transferred to an organization charged with the responsibility of absorbing overflow workload.
The ORF utilization rate for an end item will be computed by dividing the number of work orders closed out using ORF by the total number of work orders for repair that have been completed for the end item.
ORF transaction time measures a factor that impacts upon repair cycle time and the efficiency of the ORF decision process. ORF transaction time is determined by calculating, for the previous 12 months, the average of the number of calendar days between acceptance of the work order into the support maintenance activity and customer receipt of the ORF asset.
The rejection rate is the number of items being reprocessed into a commodity shop for rework, divided by the total number of items repaired.

## Slide 35: Methods to Overcome Shortfalls
Push packages
Search for substitute
Authorize controlled exchange
Lower cannibalization authorization level
Move critical components by Army air
Revise maintenance priorities
Seek support from Sustainment BDE
Cross level workload between maintenance units
Seek host nation support
Contract support
Notes: <number>
MAINTENANCE SUPPORT
ELO D
Support Operations Handbook, Fixing The Force

## Slide 36: Maintenance Operations
Notes: <number>
MAINTENANCE SUPPORT
ELO B
The type and tempo of combat affects the nature of the maintenance unit’s workload. During fast-moving offensive operations, maintenance personnel place maximum maintenance effort on preparing equipment for combat. During the offensive phase, priority will be placed on recovery, BDAR, and roadside repair, or on collecting,classifying, and reporting abandoned equipment.
Offensive operations are marked by forward movement of combat elements. As the operation moves forward, maintenance support elements join in the movement. Maintenance units must maximize repair efforts forward.
FMTs may accompany the spearhead of the attack. During the attack, the majority of the Maintenance Platoon is located in the TF combat trains area. The FMTs are forward with the maneuver companies. After the attack, the BMO coordinates maintenance requirements with the Battalion XO.

## Slide 37: Supporting Offensive Operations
Plan emphasis on BDAR
Plan a series of MCPs that are ideally collocated at or near casualty collection points
Consider splitting recovery assets to provide broader coverage for attacking companies
Ensure rapid repair and return of non-mission capable equipment to support the operation based on commander’s priorities
Send limited back-up forward to support the Field Maintenance Teams from the BSB Field Maintenance Company
Consider the use of air assets to bring critical repair parts forward
Notes: ELO B FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 10-99
FM 4-30.3, para 3-8—3-10
PLANNING FOR MAINTENANCE OPERATIONS – OFFENSE
3-8. Planners ensure maintenance operations support momentum and massing at critical points. Maintenance personnel maximize momentum by fixing inoperable equipment at the point of malfunction or damage. They enhance momentum by keeping the maximum number of weapon systems operational. Therefore, maintenance and recovery personnel perform their mission as far forward on the battlefield as possible.
3-9. Prior to offensive operations, maintenance planners should consider the following: Available maintenance units/teams, Stockage levels for repair parts, Forward placement of FMTs and the UMCP, Channels and procedures for recovery, collection, evacuation,and disposition of captured or abandoned materiel.
3-10. As the tempo of the situation and the distance involved increase, support units may have difficulty keeping pace with requirements. Maintenance support is positioned as far forward as possible, normally placing FMTs in the UMCP.
3-14. Unit mechanics accompany or follow the most forward attacking elements. Plans include recovery of weapon systems that mechanics cannot fix within established maintenance repair timelines. Maintainers use BDAR to rapidly return disabled essential equipment to the commander.
3-17. Maintenance units must maximize repair efforts forward. Unserviceable equipment requiring more than limited component replacement, adjustment, and servicing will be recovered to a centrally located MCP. The centralized MCP maximizes BDAR cannibalization and controlled exchange operations.

## Slide 38: Supporting Defensive Operations
Focus shifts to evacuation, replace forward, and fix rear
Employ on-site maintenance procedures (fix forward)
Dispatch field maintenance teams as far forward as possible to cut down on the requirement to evacuate equipment
Establish MCPs close to existing road networks to enhance the “replace forward” concept
Focus maintenance priority to support critical combat or combat support units
Notes: <number>
MAINTENANCE SUPPORT
ELO B
FM 4-30.3, Maintenance Operations and Procedures, Chapter 3-26 to 3-38
FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 10-111
FM 4-30.3, para 3-30:
PLANNING FOR MAINTENANCE OPERATIONS – DEFENSE
The primary thrust of the maintenance effort in the defense is to maximize the number of combat-ready weapon systems. Once the defensive battle begins, the thrust is to fix the maximum number of inoperable systems and return them to the battle. This requires forward
support at, or as near as possible to, the intended AO of the systems.
Supported units in the defense are not as widespread as in the offense. Maintenance support operations can therefore be more centralized. Defensive operations also do not require displacement as often as in the offense,

## Slide 39: Supporting Stability and Reconstruction Operations
Prepare to integrate contractors into your organization
Consider the use of non-standard logistics to either augment or replace existing capability
  Reduces dependence on the logistics system, improves response time, and frees airlift and sealift for other priority needs
Consider the requirements of maintaining non-standard equipment (i.e. locally purchased generators, vehicles, etc.)
Notes: ELO B FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 8-1, Chapter 8-1
FM 3-07, Stability and Support Operations, Page 2-10, Chapter 2-42
Army forces do not conduct stability and reconstruction operations within the United States. Under U.S law, the federal and state governments are responsible for those tasks.
However, maintenance units may be deployed to provide maintenance support during peacekeeping, humanitarian, or disaster relief operations. In most support operations, the U.S. military will be assisting non-governmental organizations in providing the required level of support to the affected population. The type and density of customer equipment will largely determine the modular structure of maintenance companies.
FM 1, The Army, page 49, para 3-29:
Stability and reconstruction operations sustain and exploit security and control over areas, populations, and resources. They employ military capabilities to reconstruct or establish services and support civilian agencies. Stability and reconstruction operations involve both coercive and cooperative actions. They may occur before, during, and after offensive and defensive operations; however, they also occur separately, usually at the lower end of the range of military operations. Stability and reconstruction operations lead to an environment in which, in cooperation with a legitimate government, the other instruments of national power can predominate.

## Slide 40: Supporting Civil Support Operations
Provide support to the largest number of people
Coordinate actions with other agencies
Establish measures of effectiveness
Transfer civic responsibilities to civilian agencies as soon as possible
Assess the availability of Civil Affairs, MPs, and Engineers to assist with specialized repairs
Notes: ELO B FMI 3-90.5, Heavy Brigade Combat Team Combined Arms Battalion, Page 8-33, Chapter 8-131; Page 3-38, Chapter 1-162.
FM 1, The Army, page 49, para 3-31:
Civil support operations address the consequences of man-made or natural accidents and incidents beyond the capabilities of civilian authorities. Army forces conduct civil support operations when requested, providing Army expertise and capabilities to lead agency authorities.
FM 4-30.3: 3-51. Since humanitarian missions are conducted in either friendly or hostile environments, maintenance planners must consider the situation and do the following:
• Locate maintenance operations away from dense population centers.
• Identify maintenance sites that units can easily secure and defend.
• Coordinate with engineer support for earthen barriers if required by the Base Cluster concept.
• Enclose maintenance operations areas with barrier materiel if required by the Base Cluster concept.
3-53. In disaster relief operations, maintenance and maintenance planners perform the following:
• Identify commercial vendors who can quickly supply the technical and repair parts support required.
• Organize assets from other agencies, contractors, and local maintenance resources for economy of effort.

## Slide 41: Supporting Urban Warfare Operations
Field maintenance teams must operate well forward to support units fighting in urban areas
Some maintenance operations may be consolidated in civilian facilities
Many vehicles may have to be fixed near their fighting positions
Combat in urban areas generates a high demand for tires
The dust and rough handling characteristic of combat in urban areas also places great strains on communication and night observation devices
Notes: ELO B
FM 3-06.11, Combined Arms Operations in Urban Terrain, Chapter 13-2c:
c. Fix. Maintenance teams must operate well forward to support units fighting in urban areas. Some maintenance operations may be consolidated in civilian facilities and many vehicles may have to be fixed near the fighting positions. Battle damage assessment and repair (BDAR) procedures allow mechanics to be inventive and make maximum use of battlefield damage, analysis, and repair techniques to return damaged vehicles to a serviceable condition (see applicable TMs). Other considerations include:
  (1) Combat in urban areas generates a high demand for tires.
  (2) The dust and rough handling characteristic of combat in urban areas also places
  great strains on communication and night observation devices.
  (3) The unit armorer and their small-arms repair kits provide only limited maintenance. S4s should plan for increased weapon maintenance demands and coordinate maintenance support from higher headquarters. Based on recommendations from the staff (S3, S4, and motor officer), the commander may choose to consolidate and cross level major items of equipment and weapons.
NOTE: During recent experimentation, a higher number of M16A2 and M4 rifles were rendered unserviceable due to rounds impacting on the weapons as a result of close combat during precision and high intensity engagements. CSS planners must be prepared to replace a higher number of unserviceable weapons during urban combat.