## Slide 1: FUEL SUPPORT
For additional information or to help clarify information on a slide, select View and then drop down to select Notes Page.
Notes: The AOE US Army Corps used as much fuel per day as General George S. Patton's entire Third Army used in its race across France. During the ground offensive in Operation Desert Storm, VII Corps required 2.4 million gallons of fuel daily; XVIII Airborne Corps needed 2.1 million gallons of fuel. This equated to 900 tanker loads a day. These fuel consumption and distribution requirements presented a monumental task for the fuel haulers, a task that was compounded by the extended LOC.
Obviously, fuel consumption in today’s Army is tremendous, whether we are operating in a desert or jungle environment. Getting the right amount of bulk fuel to the right place at the right time is a major sustainment challenge for SPO staff officers.
Fuel is a critical demand commodity when supporting HBCTs that are 100% mobile. The HBCT retains 100% mobility by storing its three replenishment loads of fuel in internal mobile fuel platforms. However, the HBCTs must be resupplied.
What makes the bulk fuel function unique for fuel planners and managers is not only the product but also the assets required to move, store and distribute bulk fuel.

## Slide 2: TLO and ELOs
Terminal Learning Objective: Describe the missions, capabilities, and operational considerations for bulk fuel support
Enabling Learning Objectives:
A. Describe the missions, capabilities, and employment of modular fuel support organizations and the interface of fuel distribution managers in fuel support operations in the contemporary operating environment (COE).
B. Diagram the distribution flow and overall concept of fuel supply operations
C Discuss considerations for planning bulk fuel storage and distribution
D. Describe storage and distribution systems available for bulk fuel
E. Identify and discuss considerations for estimating fuel requirements
F. Discuss operational lessons learned
Notes: Your objectives for this lesson are listed on this slide.
After reviewing these slides, you will check your understanding of these learning objectives by answering the questions in the checks on learning quiz that accompanies this lesson.

## Slide 3: REFERENCES
Modular Force References
FM 3-0, Operations, Jun 2001
FM 3.06.11, Combined Arms Operations in Urban Terrain, Feb 2002
FMI 3-90-6, Heavy Brigade Combat Team, Mar 2005
FM 4-20, Quartermaster Operations, final draft 2003
FMI 4-90.1, Heavy Brigade Combat Team Logistics, Mar 2005
FM 4-93.2, The Sustainment Brigade, Cord Draft Oct 2005
Center for Army Lessons Learned (CALL) Army Transformation (SBCT & Modular Force) site
AOE References
FM 54-30, Corps Support Groups, Jun 93
FM 63-2-1, DISCOM, Light, Airborne, and Air Assault Division, Sep 94
FM 63-3, Corps Support Command, Jun 93
Notes: To remain current with modular force doctrine, recommend that you maintain a link with the Center for Army Lessons Learned (CALL) website for Army Transformation (SBCT & Modular Force) at:
https://call2.army.mil/focus/transformation.
Interim modular force field manuals (FMIs) are maintained on this web site.

## Slide 4: ACRONYMS
GPD: gallons per day
HBCT: heavy brigade combat team
HEMTT-LHS: heavy expanded mobility tactical truck- load handling system
PLS: palletized load system
FMTV: family of medium tactical vehicles
BSA: brigade support area
BSB: brigade support battalion
CABSA: combined arms battalion support area
DC: distribution company
FSC: forward support company
Notes: The majority of the new acronyms listed on this slide are the result of changing to a modular organization based on support to the HBCT.

## Slide 5: OUTLINE
Fuel support fundamentals
Fuel planners and managers
Modular fuel organizations
Fuel distribution
Supporting offensive, defensive, and urban operations
Notes: Again, your focus will be support of the HBCT. You will focus on the key bulk fuel distribution planners and managers and on the modular force that provides bulk fuel support to the HBCT.
Once again, you must first review the basic fundamentals of bulk fuel support before you proceed to focus on the key planners and managers in the modular organizations that distribute bulk fuel.

## Slide 6: FUEL SUPPORT FUNDAMENTALS
Notes: Bulk fuel support fundamentals include the mandate for a single-fuel battlefield.
SPO staff must consider the unique distribution requirements presented by bulk fuel. The fuel distribution methods (supply point, unit distribution, and throughput) are similar to those employed in the distribution of general supplies.
Previously you have studied forward logistics point (LRP)/ forward logistic element (FLE) in previous lessons as techniques of providing forward supply support. You must now learn about refuel-on-the-move (ROM) and tactical refueling (TF) as techniques that help to ensure 100% mobility of HBCTs and maintain the momentum of the attack.

## Slide 7
SINGLE-FUEL BATTLEFIELD
JP8
Increases flexibility to refuel air and ground equipment
Eliminates separate storage and distribution systems
Some Joint, coalition, HNS, and Army
equipment may require diesel or MOGAS - UAVs - Some USAF Aircraft - Contracted Vehicles & HNS - Some generators and stoves
Notes: <number>
SUPPLYING FUEL
ELO C Reference: Joint Publication 4-03, Joint Bulk Petroleum and Water Doctrine, 23 May 2003
pp II-8 para 10b: Primary fuel support for land-based air and ground forces in all theaters shall be accomplished using a single kerosene-based fuel, in order of precedence: JP8, commercial jet fuel (with additive package), or commercial jet fuel (without additives), as approved by the combatant commander.
Reference: JP-8, The Single Fuel Forward
JET A-1 is the commercial industry standard for aviation fuel and is available worldwide. JET A-1 is essentially identical to JP-8 except that it does not necessarily contain the three additives required in JP-8. (Fuel System Icing Inhibitor, corrosion Inhibitor, and static dissipator. (pp4)
Question: Are other nations using JP-8 as a ground fuel? Yes. France, United Kingdom, Norway, and the Netherlands as well as the United States show NATO Code Number F-34 (i.e., JP-8) as an acceptable alternate for NATO Code Number F-54 (i.e., our DF-2). (pp16)
Question: Will using either JP-8 or JP-5 plug fuel filters on vehicles? No.
Both JP-5 and JP-8 are inherently cleaner fuels when compared to diesel fuel, and they will not therefore cause fuel filter plugging. (pp18)

## Slide 8
FUEL DISTRIBUTION CONSIDERATIONS
Mission, size, and composition of the supported force
Commander’s intent
Terrain
Resources available
Mode of delivery
Force requirements (including joint forces)
Petroleum supply and DS units required
Seasonal requirements
Notes: <number>
SUPPLYING FUEL
ELO C Reference: FM 63-3, Ch 6 (except for the joint requirement)
Reference: Joint Publication 4-03, Joint Bulk Petroleum and Water Doctrine, 23 May 2003
pp II-7 para 9a: The Army normally provides management of overland petroleum support, including inland waterways, to US land-based forces of all DOD components.
pp II-7 para 9b : The Air Force shall provide distribution of bulk petroleum products by air within a theater where immediate support is needed at remote locations.
pp II-7 para 9c: The Navy shall provide seaward and over-the-shore bulk petroleum products to the high-water mark for US sea- and land-based forces of all DOD components.

## Slide 9
FUEL DISTRIBUTION METHODS
Supply Point Units must pickup
  BSA
  FLB
Unit Distribution Supplies are delivered to using units
  LOGPAC
Throughput Bypass one or more echelons to issue as far forward as possible
  Sustainment BDE to BSA/CBT Trains
Notes: <number>
SUPPLYING FUEL
ELOs C & D FM 4-20, Methods of resupply, para 6-37
The three distribution methods of re-supply are:
Supply Point: Supply point distribution requires unit representatives to move to a supply point to pick up their supplies. Fuel is provided to supported units for the most part using supply point distribution. A schedule for issue of bulk fuel to the units in the brigade area at the FSC Class III point is coordinated between the supported brigade S4, the BSB SPO, and the FSC. Supported units pick up fuel in their organic refueling vehicles, and authorized unit representatives sign for quantities received. Issue documents are used to provide input to the daily status report. They are abstracted daily to the monthly abstract of issues.
Unit: Unit distribution provides delivery of supplies directly to the unit. A unit representative meets the re-supply package at the logistics release point (LRP) and guides the re-supply to the supported unit’s position. Distribution to individual units is conducted only when necessary, based on status, OPTEMPO, and commander priorities.
Throughput: Throughput distribution to forward areas bypasses one or more echelons in the supply system to minimize handling and speed delivery forward. This method best facilitates distribution velocity.
NOTE: Throughput will be maximized down to the BSA, and down to lower levels on a case-by-case, exception, or mission dependent basis. Due to EAB time/distance factors, OPTEMPO, and the challenges in synchronizing deliveries forward, this throughput to the lowest level will be coordinated through support operations channels.

## Slide 10
Refuel-on-the-Move (ROM)
  Refuel combat vehicles using DS assets
  Increases BN’s range and time on the objective
  Does not reduce bulk quantity in organic supply vehicles
Forward Logistics Element (FLE)
  Supports fast-moving offensive operations over significant distances
  Reduces turn-around time for BN organic assets
  Can function as the lead element of BSA move providing responsive fuel support
FUEL TECHNIQUES
Tactical Refueling (TF)
  Support provided by FSC HEMTTS
  Provided every 6-8 hours
  Allows for continued offensive movement
Notes: <number>
SUPPLYING FUEL
ELOs C & D Fuel Techniques Reference: FM 54-30, Ch 8; FM 63-2-1, Ch 6
Forward Logistics Element (FLE). The FLE can get critical Class III closer to supported units without taking the time it requires to move the entire support area. This allows units to get key support without having to go all the way back to the support area. The FLE can also function as the lead element of a support area move. In this role, the FLE provides continuous support while the rest of the FSC elements move. Task organizing a multifunctional FLE from FSC assets to operate from a FLB may be appropriate to support:
Fast moving offensive operations over significant distances.
Early phases of contingency operations.
Units geographically separated from the other units supported by the FSC.
Refuel-on-the-Move (ROM). ROMs ensure that the fuel tanks of combat and fuel-servicing vehicles are refueled enroute. The purpose of a ROM is to provide rapid refueling for combat vehicles based on time to maintain momentum in the offense. ROM operations are normally conducted from behind the brigade rear boundary. FSCs use 5K tankers, HEMTT refuelers, and refueling equipment to establish a refueling site. Set up as a retail service station, vehicle fuel tanks are topped off as they pass the supply point. A ROM can be set up along any portion of a line of march. Using DS assets eliminates the need to draw down petroleum supply vehicles organic to combat units. The ROM kit is an asset to be used for tactical refueling of maneuver units. It has no storage capabilities. ROM kit can dispense 20K‑24K gallons per hour at 35 GPM on 8 points. Requirements: 400 feet and 10 Soldiers to operate one 8 point ROM.
BCT S4 coordinates the ROM.
BCT S3 & S4 determine the general location, but the BSB determines the exact site.
BCT S4 provides march tables, fuel forecasts and vehicle densities.
NOTE: Plan for one ROM site per BSB and plan for night ROM.
Tactical Refueling. The FSCs may move fuel forward to a tactical refueling point to ensure combat vehicles deploy to the battle with full fuel tanks. One technique which has worked in fuel resupply operations involves the use of FSC tankers in combination with maneuver battalion HEMTTs or TPUs. One tanker deploys with two TPUs or HEMTTs to form a refueling module that can service four combat vehicles at a time. Up to six modules can be set up together to service a task-organized company team, if sufficient tankers are available and the tactical situation permits. Refuel sites can be set up on MSRs either in a single site, which can service up to 24 vehicles at a time, or in a split-site configuration to stagger march elements and reduce traffic congestion. The maneuver battalion, which is familiar with the area, is responsible for site selection and security. The battalion S4 coordinates with the FSC on where and when the refueling operation will be and how much fuel is required. The primary benefit of this technique is speed. It takes 5 minutes for the FSC tanker driver and assistant driver to deploy one section of a 50-foot hoseline to the T-valve, start the pony engine, and be prepared to pump into the TPUs or HEMTTs.

## Slide 11: FUEL PLANNERS AND MANAGERS
Notes: FM 4-90.1, para 6-44.
While consumption rates are predictable, bulk fuel consumption requirements will be significant and require almost constant contact with the supported units. The SPO and his staff form the key interface between the supported units and the support battalion.
As an officer on the BSB SPO/Sustainment Brigade SPO/DMC staff or assigned to the Supply and Services Cell of the BSB SPO, what are your responsibilities for managing fuel distribution? Who will you coordinate with to ensure that bulk fuel requirements are met?
Basically, fuel forecasts are projected for future tactical operations. The Brigade S4, in coordination with the BSB support operations staff, submits a forecast to the Sustainmnet Bde SPO/DMC for bulk fuel requirements of all supported units in the brigade area.
The FSC petroleum section submits a daily status report to the Spt Ops Officer on bulk fuel quantities received, issued, and on hand. The BSB SPO then submits a roll up report to Sustainment Bde SPO/DMC.

## Slide 12: Sust Bde SPO/DMC & BSB SPO
Notes: ELO A
SPO staff form the distribution management support element for the brigade. They function as a distribution management center (DMC) does in other organizations
Always remember that the Support Operations Section is focused on external support misssion. The BSB’s battle staff are concerned with the internal functioning and support of the BSB. The SPO advises the commander on bulk fuel support requirements versus support assets available.
Sust Bde SPO/DMC Fuel Tasks:
  Maintains bulk fuel stock status
  Consolidates support unit’s requirements for bulk fuel
  Forwards bulk fuel requirements to the theater support command (TSC)
  Synchronizes throughput distribution of bulk fuel with BSB SPO
The Sustainment Bde’s Petroleum-Water Branch controls and manages the bulk fuel and water supply to the supported elements. It directs the receipt, storage, inspection, testing, issue, distribution, and accountability of bulk fuel and water stocks for the AO/JAO.
BSB SPO Fuel Tasks:
  Manages and controls BCT bulk fuel stocks
  Forwards bulk fuel requirements and forecast to SUS BDE SPO Supply/Services Division
  Directs distribution of CL III(B) in BCT
  Maintains bulk fuel status
  Coordinates/synchronizes inbound bulk fuel

## Slide 13: BSB SUPPORT OPERATIONS CELLS
Maint Cell
Sup & Svc Cell
Trans Mgt Cell
HHS Cell
Ammo Cell
Contract Cell
BSB SPO establishes standard push requirements based on:
  Past consumption
  Bulk storage capabilities
  Bulk distribution capabilities
  Resupply turn around times
SPO
Notes: ELO A Fuel Managers Reference: FMI 4-90.1, Para 3-46
The BSB support operations staff are responsible for coordinating the resupply of bulk fuel to the forward support companies (FSCs) and the BSB Distribution Company. They consolidate the bulk fuel status reports for the brigade and slice elements and submit them to the Sustainment Brigade SPO.
The Supply and Services Officer forecasts and monitors the distribution of supplies within the brigade. He is supported by a Petroleum/Water Officer.
Supply and Services Officer Duties:
Determines petroleum and water requirements.
Provides technical expertise on supply and distribution of petroleum and water.
Reviews bulk fuel forecasts and adjust the forecasts after coordination with the brigade S3 on the impact of tactical operations on fuel requirements.
Secures additional fuel and water storage capacity.

## Slide 14: FUEL PLANNERS
The HBCT S4 and BSB SPO forecast fuel requirements for the HBCT
Forecasts for fuel usage are sent from the BSB support operations center to the Sustainment Brigade SPO
HBCT S4 and BSB SPO predict future needs based upon current operations, FMC rates, density of equipment, and historical data
Bulk fuel will be issued based on priorities established by the HBCT S4 with guidance from the HBCT commander
The BSB SPO coordinates resupply of bulk fuel to the FSCs and the BSB Distribution Company
The FSC CP and the BN S4 will coordinate the refueling site and quantity of issue for the maneuver or other supported companies
Notes: ELO A Reference: 4-90.1 para 6-2
This slide lists the key fuel planners and their interface with other key planners and managers.
Division/corps planners forecast fuel requirements for the HBCT. Forecasts for fuel usage are received by the division support operations center from the BSB support operations center.
6-43. Bulk fuel will be issued based on priorities established by the HBCT S4 with guidance from the HBCT commander.

## Slide 15
REQUIREMENTS COMPUTATION METHODS
Historical Data
  Most accurate, if appropriate data is available
Equipment Consumption
  Computes for a particular unit based on equipment, hours, and distance
Combat Profile
  Hourly usage rates for combat vehicles
  Miles usage rate for wheeled vehicles
  Pound burn rate for aviation assets
Gallons-per-Person-per-Day
  Used early in deployment; seldom used below theater
Notes: <number>
SUPPLYING FUEL
ELO E Fuel Fundamentals Reference: FM 4-20, Para 11-31
Accurate fuel requirements are essential in designing an effective fuel distribution system. To compute or determine petroleum requirements for a unit, several methods are used. These methods are used alone or in combination. The choice depends upon time, distance, weather, geography, personnel, and type of mission.
The Methods:
1. Historical Data. This is the most accurate method. It uses information from previous AARs of a similar mission. Terrain, weather, organizational strength, vehicles, and equipment should remain constant.
2. Equipment Consumption. Used to compute the equipment consumption requirements for a particular unit. Information required include: type, fuel usage, usage rate, and density of each piece of equipment, equipment density, amount of fuel consumed by type of equipment, and usage rates.
3. Combat Profile. Used for combat vehicles only. This is the 2d most accurate method. It produces an accurate forecast of the consumption rate and is based upon hourly usage factors. This method is a refinement of the equipment consumption method. It uses actual projected hours instead of tables.
4. Gallons/man/day. Used in the early planning stages when no definitive information is available on the number and types of vehicles. This method is seldom used below corps level. This method is used only as a guide and is not a substitute for exact consumption data.

## Slide 16: FUEL ORGANIZATIONS
Notes: Your focus is on the HBCT’s fuel distribution organization (FSCs and BSB Distribution Company). However, you must also acknowledge the QM/petroleum supply unit and truck companies of the division/corps sustainment brigade that will provide the bulk fuel and tankers to transport the fuel to the brigade AO.

## Slide 17
Key Task
ISG Reports Log Requirements to CTCP
Bn S4 Consolidates Bn Req & Passes to FSC
FSC Key Fuel Task
Manages / C2s Stocks For BN
XO Directs General Supply Sect To Support
Push Sent To LRP On LOGPAC
OH Bal Rpt & Forecast Sent To BSB SPO
Distribution CO Key Fuel Task
DC Retains DS Stocks for BCT
DS Stocks Controlled By BSB SPO
BSB SPO Directs DC to Replenish FSC Stocks
Stock Status Sent to BSB SPO Daily
Coordinates with BSB SPO for Receipt Of Division Through-Put
CL III Sect Executes Msn
Systems Used: HEMMT 2.5k Tankers
Fuel Systems: M969 5k Tankers
Sustainment BDE Key Fuel Task
Maintains Stock Status
Consolidates Div Requirement
Forwards to Division and TSC
Synchronizes Through-Put Distribution
BDE SPT BN Key Fuel Task
BSB SPO Manages & C2s BCT Stocks
Forwards Forecast to DMC Supply/Services
Direct Distribution of IIIB In BCT
Maintain Stock Status
Forecast Requirements
Forward Requirement to DMC
Coordinate/Synchronize Inbound Receipts
FUEL DISTRIBUTION UNITS
Notes: <number>
SUPPLYING FUEL
ELO A Reference: FM-I 4-90.1 Heavy Brigade Combat Team Logistics, Para 6-42
This slide displays the key bulk fuel distribution organization, to include the Sustainment Brigade, the BSB, its Distribution Company, and the FSC. More importantly, it lists the key fuel tasks performed at each of these organizations.
Of note, the HBCT retains its mobility by storing its three replenishment loads of fuel in internal mobile fuel platforms (one combat load each at the using unit, the FSC, and the BSB), thereby eliminating the need for on-ground storage.
Therefore, the corps/division sustainment brigade must resupply the HBCT with bulk fuel. Following throughput distribution principle, a transportation medium truck company usually makes deliveries directly to the HBCT.
If you are assigned to the BSB SPO, you will coordinate bulk fuel distribution into the brigade in coordination with the HBCT S4.

## Slide 18: BSB, DC: Fuel & Water Platoon
Provides reinforcing Class IIIB resupply to the FSCs (one combat load for the HBCT) and area support to brigade units.
Provides retail fuel capability to individual vehicles of the BSB.
Provides supply point distribution to other units within the BSA.
Class III(B) Section Mission
SUP
PLT HQ
FUEL/
WATER
CO HQ
TRANS
PLT
FUEL/
WATER
CL III
PLT HQ
Water
Notes: ELO A Modular Fuel Organizations Reference: FM-I 4-90.1, Heavy Brigade Combat Team Logistics, Para 3-110
The BSB Distribution Company provides DS support to the BTB and backup/reinforcing support to the FSCs. The BSB’s Distribution Company provides unit distribution to the FSCs, based on fuel consumption, distances, and METT-TC.
Distribution Company Key Fuel Tasks:
Retains stocks for BCT
Report stock status to BSB SPO daily
Coordinates with BSB SPO for receipt of throughput fuel resupply
DS stocks are controlled by BSB SPO
BSB SPO directs Distribution Compay to replenish FSC stocks

## Slide 19: BSB, DC, Fuel & Water Platoon: CL III Section
Key Tasks:
Sends stock status to BSB SPO daily
Coordinates with BSB SPO for receipt of throughput from Sustainment BDE
Class III section delivers to FSC
4 Truck Squads
Notes: ELO A Reference: FM-I 4-90.1 Heavy Brigade Combat Team Logistics, para 3-102, -103, -110
3-110. The Class III section, Distribution Company, BSB, provides reinforcing Class III (B) resupply to the FSCs (one combat load for the HBCT), and area support to brigade units. This section also provides supply point distribution to other units within the BSA.

## Slide 20: FSC Distribution Platoon
Key Tasks:
FSC CP and the BN S4 will coordinate refueling site and quantity
Provide bulk fuel status to BN S4
FSC conducts tactical refueling for maneuver companies.
Dist
PLT
Plt HQ
CL V
CL III
Section
Gen Sup
Section
FSC
FSCs are assigned to the BSB but OPCON to each maneuver battalion
Notes: ELO A Reference: FM-I 4-90.1 Heavy Brigade Combat Team Logistics, Para 6-43
The FSC CP and the BN S4 will coordinate the refueling site and quantity of issue for the maneuver companies. Fuel HEMTT tankers located in the FSC accomplish the tactical refueling operations for the maneuver companies. The FSC moves to a designated site and fuels the combat platforms within the HBCT.
To optimize bulk fuel storage capacity forward and ensure HEMTT tankers have smaller turns to refuel, the BSB commander has the flexibility to position BSB DC HEMMT fuelers in the FSC's field trains location.
HEMTT authorization varies depending on the FSC:
CAB FSC
  12 2.5k HEMTT
  1 TPU (3 pods)
FIRES FSC
  4 2.5k HEMTT
  1 TPU (3 pods)
RECON FSC
  3 2.5k HEMTT
  1 TPU (3 pods)

## Slide 21: FSC EMPLOYMENT
Brigade Support Area
Combined Arms Battalion Support Area (CABSA)
FSC Forward
Combat Trains Command Post (CTCP)
0.5 to 1 km
1-4 km
10-14 km
FSC
Emergency CL III(B) echeloned forward HEMTT Tankers or TPUs
FSC CDR/1SG
Bn S4/S1
Co 1SG
Co 1SG
Co 1SG
Co 1SG
LRP
Company Supply Sergeants build the LOGPACs
Distribution Platoon Leader leads the LOGPAC to the LRP
Notes: ELO A Reference: FM-I 4-90.1, Heavy Brigade Combat Team Logistics, Fig. 5-4
6-331.The most efficient re-supply of tactical units is accomplished by logistics packages (LOGPACs). LOGPACs are organized in the field trains’ area by the company supply sergeant under the supervision of the FSC commander and the distribution platoon leader. LOGPACs move in the combat logistics patrol, normally under the control of the distribution platoon leader.
The S4 must plan and coordinate sustainment operations to ensure that they fully support the commander's tactical plans. The battalion SOP establishes the standard LOGPAC and how the sustainment mission is executed via the combat logistics patrol.
6-335. When FSC LOGPAC preparations are complete, the CTCP advises the company. When the company portion of the FSC’s LOGPAC has been formed, it is ready to move forward under the control of the company supply sergeant. The FSC’s distribution platoon leader normally organizes a combat logistics patrol for movement of all company LOGPACs under his control; in emergencies, he dispatches unit LOGPACs individually.
The LRP is a linkup point on the ground where the company’s LOGPACs, led by the company supply sergeants, are met by the unit 1SG or unit guide from the individual company trains i.e. someone familiar with the terrain, current tactical situation, and route to the company trains location. The escorts from the companies arrive at the LRP early and take a concealed position near the LRP where they can quickly identify the LOGPAC as it moves toward the LRP.
6-338. The individual company LOGPACs do not stop but roll through the LRP, picking up the escort and moving toward the individual companies. From the LRP, the company first sergeant or guide controls the LOGPAC and conducts re-supply as described in FM 3-90.1. The unit first sergeant informs his supply sergeant of requirements for the next LOGPAC. The supply sergeant collects outgoing mail, personnel, and equipment for movement back to the support area. The LOGPAC then follows the unit SOP and returns to the LRP, field trains’ location, or battalion support area.
The FSC CP and the BN S4 will coordinate the refueling site and quantity of issue for the maneuver companies. Fuel HEMTT tankers located in FSC accomplish the tactical refueling operations for the maneuver companies. To optimize bulk fuel storage capacity forward and ensure HEMTT tankers have smaller turns to refuel, the BSB commander has the flexibility to position BSB DC HEMMT fuelers in the FSC's field trains location.

## Slide 22: FUEL DISTRIBUTION
Notes: Fuel forecasts are based on future tactical operations. Bulk fuels are not formally requested.
The Brigade S4 in coordination with the BSB support operations section submits a forecast for bulk fuel requirements of all units in the brigade area to the SUS Bde SPO/DMC.
The FSC petroleum section submits a daily status report on quantities received, issued, and on hand to the BSB SPO who submits it to SUS Bde SPO/DMC.

## Slide 23: BULK FUEL DISTRIBUTION
Bulk fuel is distributed to the Sustainment Brigade for forward distribution to the HBCT.
The HBCT retains 100% mobility by storing its three replenishment loads of fuel in internal mobile fuel platforms.
  One combat load (CL) at the unit
  One CL at the FSC
  One CL at the BSB
Notes: ELO A FMI 4-90.1, para 6-38 & 6-42
Units maintain a prescribed load of fuel to allow them to operate until the system can resupply them. They use organic equipment to receive the product and refuel their vehicles
The HBCT retains its mobility by storing its three replenishment loads of fuel in internal mobile fuel platforms (one combat load each at the using unit, the FSC, and the BSB). This eliminates the need for on-ground storage.
The goal of bulk petroleum distribution management is to keep storage tanks full. Resupply from the sustainment brigade to the HBCT will be conducted, as required, to maintain combat readiness.

## Slide 24: DISTRIBUTION OPS SEC, BSB SPO
Key Tasks
BSB SPO manages & controls BCT stocks
FSCs forecast to DMC supply/services div
Directs distribution of Class III(B) in the BCT
Forecasts requirements for the BCT to DMC
Maintains stock status
Coordinates/synchronizes inbound fuel
SPO establishes standard push requirements based on:
  Past consumption
  Bulk storage capabilities
  Bulk distribution capabilities
  Resupply turn around times
Notes: ELO A
The BSB support operations, with guidance from the HBCT S4, will coordinate bulk fuel distribution in the brigade.
If METT-TC prohibits forecasting, standard prearranged shipments may be sent on a regular basis to the FSCs. These would continue until the brigade S4 or Spt Ops Officer requests a change

## Slide 25: FUEL RESUPPLY SUMMARY
The HBCT S4 and BSB SPO analyze current consumption rates, historical data, and future operations to predict future needs.
Their fuel forecasts are received by the Sustainment Brigade support operations center.
The Sustainment Brigade (petroleum support company) and POL transportation battalions deliver Class III(B) to the BSB.
The BSB distribution company delivers Class (IIIB) to the forward support company.
The FSC fuel tankers conduct tactical refuel for the maneuver companies.
Notes: ELO A Reference: FMI 4-90.1 Heavy Brigade Combat Team Logistics,
- Para 6-1: Fuel HEMTT tankers located in each FSC accomplishes the tactical refueling operations for the maneuver companies.
- Para 6-2: The HBCT S4 and BSB SPO … analyze current consumption to predict future needs.
Forecasts for fuel usage are received by the division support operations center from the BSB support operations center.
Para 6-3: Division fuel operations consist of SRO and mission staging operations (MSO) [FSCs conduct CRO], using ground truck assets coming out of the sustainment brigade (petroleum support company), and POL transportation battalions. In SRO, elements from the BSB move to top-off units within the FSC. Both of these actions are conducted within the HBCT battle space by organic HBCT assets.

## Slide 26: Fuel Distribution Process
Notes: ELO A Reference: FMI 4-90.1, Para 3-45 to 49
The petroleum support base serves as a hub for receiving, temporarily storing, and moving fuels to Petroleum Support Companies (PSCs) in the corps and division sustainment brigades. [NOTE: Since the sustainment brigade doctrine is still being developed, the support organization and the actual names of the companies assigned/attached to the sustainment brigade may differ slightly.] Petroleum support battalions in the corps sustainment brigade provide theater stocks and deliver fuel forward to the division sustainment brigade’s PSCs. The division sustainment brigades push fuel to the BSBs using ground truck assets coming out of the sustainment brigade PSC and POL transportation battalions. PSCs in the division support the area distribution mission, and POL truck companies deliver fuel to the BSB in the BCTs. QM petroleum units will provide fuel support for all US (and potentially coalition) land-based forces. Sustainment brigades, specifically QM petroleum units, will be involved in the distribution from the refinery or terminal to the BSB’s distribution company A transportation medium truck company usually makes deliveries directly to the HBCT.
Logistics Release Point (LRP). The preferred method of fuel distribution is via LRP operations, coordinated with the BSB support operations. The individual company LOGPACs do not stop but roll through the LRP, picking up the escort and moving toward the individual companies.
The BSB SPO is responsible for coordinating the resupply of bulk fuel to the FSCs and the BSB DC.

## Slide 27: SUPPORTING OPERATIONS
Notes: Today’s military consumes large quantities of petroleum products in support of combat operations. Any interruption in the flow of fuel could have a devastating effect on the Army’s ability to dominate the conflict.

## Slide 28
Plan for increased fuel consumption
Employ ROM operations to refuel combat vehicles
Build up fuel in forward locations
Arrange to throughput bulk fuel to supply points in the BSA/FLB
Plan for refueling operations as far forward as possible in covered and concealed locations
SUPPORTING OFFENSIVE OPERATIONS
Notes: <number>
SUPPLYING FUEL
ELO F Offense Fuel Operations Reference: FM 54-30, Ch 8, pg 8-12/13; Call Newsletter No. 92-X
Fuel requirements are highest in the offense. To handle high fuel consumption, forward stocks are built up and Class III points prepared LOGPACS to move forward rapidly or set up forward tactical refuel points.
6-363. Class III (B). Immediate resupply of Class III (B) is critical in offensive operations. Some planning considerations include the following:
􀁺Ensure all units are topped off with fuel and are carrying their basic load of POL
package products prior to execution.
􀁺Ensure all forward stocks are re-supplied and the Class III point is prepared to
move forward rapidly.
Set up tactical refueling points and refuel-on-the-move (ROM) sites.
􀁺Plan refueling operations based on the consumption estimates for each individual
battalion and squadron and smaller HBCT units.
􀁺
ROM support ensures that the fuel tanks of combat and fuel servicing vehicles are refueled en route based on time, not gallons. A ROM can occur along any portion of a line of march.

## Slide 29
Plan for decreased fuel consumption
Plan for and allocate additional Class III during the preparation phase
Ensure units replenish basic loads
Plan for routine resupply using LOGPAC
Plan alternate supply routes
Arrange to prestock 500-gallon drums (blivets) at successive defensive positions
SUPPORTING DEFENSIVE OPERATIONS
Notes: <number>
SUPPLYING FUEL
ELO F Defense Fuel Operations Reference: FM 54-30, Ch 8
When out of contact, supported units may continue to send vehicles back to DS Class III supply points. Alternately, they could remain in place while tankers from unit trains go forward to each vehicle position. Regardless, to decrease enemy detection, resupply should occur during periods of limited visibility.
As previously mentioned, bulk fuel carriers must remain full always. Therefore, basic load replenishment is a high priority when supporting the defense.
Commanders must weigh the risk associated with forward resupply against providing fuel from a supply point in the BSA. Supported commanders must also accept the chance of loss due to enemy actions and preplan destruction of prestocked fuel to prevent capture.

## Slide 30: SUPPORTING URBAN WARFARE
Reduced requirement (usually)
Less significant for M1 (Turbine)
POL may be available locally (local gas stations and
garages)
Quality is uncertain (poor
quality or contaminated)
Coordinate for fuel
testing
Power generations
requirements
Planning
Notes: <number>
SUPPLYING FUEL
ELO F Reference: Marine Corps Warfighting Publication (MCWP) 3-35.3, Military Operations on Urbanized Terrain (MOUT)
Bulk fuel needed by forces during combat in built-up areas is greatly reduced. (para 5102(b), pp5-1)
In open terrain, a vehicle that has run out of fuel can be recovered later. In built-up areas, the same vehicle is probably going to be lost quickly. Leaders should plan for and provide the means of moving limited amounts of bulk fuel forward to combat units. (para 5102(b), pp5-1)
Supplies of bulk Class III items and some prepackaged POL may be available at local gas stations and garages. These may be contaminated or of poor quality. . . Coordinate to have fuel tests performed. (para 5103(c), pp5-30
Reference: FM 3.06.11, Combined Arms Operations in Urban Terrain, 28 FEB 2002, CH 13, Combat Service Support
  2nd bullet -- Less significant for M1 (turbine) because the M1 burns a lot of fuel just idling.

## Slide 31: SUPPORTING URBAN WARFARE
Resupply difficult within urban environment
  Risk to bulk fuel carriers
  Rubble blocks routes
  Security
Shorter distances
Less cross-country travel
Distribution
Notes: <number>
SUPPLYING FUEL
ELO F Reference: FM 3.06.11: Combined Arms Operations in Urban Terrain, 28 FEB 2002, CH 13, Combat Service Support
Reference: RAND Corporation, On the Shoulders of Atlas: Urban CSS Operations; Russell W. Glenn, Steven Hartman, Scott Gerwehr; DRR-2894-A; October 2002; Prepared for: The United States Army
Innovative CSS leaders might be able to complement traditional methods with several ad hoc initiatives, given that urban areas are often locations in which large quantities of fuel are stored. Ports, airfields, and commercial petroleum handling facilities can be designated as early targets for seizure, either to allow friendly forces to use the fuel on hand (after testing for suitability) or for storage of imported petroleum, oil, and lubricant (POL) products. (PP57)
One U.S. Army system that is an obvious candidate . . . is the currently available Assault Hoseline System (AHS), a bulk fuel distribution capability able to traverse a wide variety of terrain types. The AHS consists of 14,000 feet of 4-inch collapsible hose and a pressure regulated pumping assembly that relies on a 350-GPM diesel pump. It can be suspended over gaps of up to two hundred feet. (PP59)
Reference: Marine Corps Warfighting Publication (MCWP) 3-35.3, Military Operations on Urbanized Terrain (MOUT)
Bulk fuel may have to be brought forward from fuel tankers by using 5-gallon cans. One can carry a fuel can long distances, even over rubble, if it is lashed to a pack frame. (para 5103(c), pp5-3)

## Slide 32: SUPPORTING URBAN WARFARE
Several small storage sites offer greater redundancy and survivability
Storage sites should:
  Offer easy access
  Not endanger other operations in case of fire
Storage
Notes: <number>
SUPPLYING FUEL
ELO F Reference: RAND Corporation, On the Shoulders of Atlas: Urban CSS Operations; Russell W. Glenn, Steven Hartman, Scott Gerwehr; DRR-2894-A; October 2002; Prepared for: The United States Army
“ . . .several small sites are preferred to one or two larger storage or distribution points so as to minimize the operational consequences should one such point be destroyed. (PP57)
Storing fuel in one location and running hoses from that point through sewer systems, buildings, or other concealed routes to supply interior or exterior storage or fueling points would further enhance security. Subterranean fuel leakage will present a danger of explosion barring proper venting, the use of spark suppressing gases, or other safety procedures. (PP 58)
CSS leaders will have to find locations that provide ready access and egress for both fuel delivery and distribution, locations that can be secured without too great a cost in manpower, and that will not unnecessarily endanger other facilities or personnel during either normal operations or in the case of fire. (PP57)

## Slide 33
OPERATIONAL LESSONS LEARNED
5-gallon cans are versatile and valuable
Consider non-doctrinal fuel storage and distribution methods
Mobile FAREs and CH47s equipped with fuel bladders offer flexibility
Find unused ROM kits
Host nation fuel sources and considerations (assault hose line)
Power requirement pulled from power grid
Notes: <number>
SUPPLYING FUEL
ELO F Fuel Lessons Learned
5 gallon cans: Every vehicle should be resourced with a minimum of two 5-gallon cans. Do the math in garrison and maintain these—they don’t have to be pretty. Also, maintain a 10% overage of caps for your cans. A large number of cans in combat become unserviceable due to a missing or broken cap.
Ingenuity: In ODS, uncommitted task force vehicles were outfitted with fiberglass water tanks (filled with fuel) to support 24ID (M) movement into Iraq—fuel from these tanks was sucked into empty M978 HEMTTs via the M978’s internal pump. This was a huge factor in allowing the division to maintain the initiative and not wait on logistics to catch up to it.
FATCOWs: CH-47 with tanks/pump in its bay. Capable of tranporting small quantities of fuel to austere locations to support elements in contact on the ground. FATCOW was used extensively as a mobile FARP in Afghanistan to support small numbers of Apache’s providing close air support to forces engaged during Operation Anaconda.
HTARS/ROM kits: When running a FLE, ROM, or mobile filling station, some of these kits are invariably not being used within the division. Find out where they are at and use them to increase your element’s capability.
Theater Logistics Handbook, CH 9 HEMTT Tanker Aviation Refueling System (HTARS)
The HTARS is a kit that consists of enough hoses, fittings, and nozzles to expand the HEMTT tankers capability to hot refuel up to four helicopters simultaneously using the on-board fuel-servicing pump. The equipment is lightweight, has manually operated controls, and is equipped with valved and swivel adapters that allow connections between camlock and unisex type fittings. This equipment can be used in forward areas. It can be transported in the storage box of the HEMTT tanker.
Host nation fuel: Use an assault hose line to generate a stand-off distance from your host-nation download point to your storage equipment.
Captured fuel: Evaluate future theaters carefully. Kandahar Airfield had a 500,000 gallon underground storage tank that was nearly full when OEF1 forces occupied the airfield. The fuel was not sufficient for ground and air vehicles due to excessive contaminants. However, it was used to run some generators.