## Slide 1
MULTI-FREQUENCY OBSERVATIONS USING MULTIFEED SYSTEMS
ALESSANDRO ORFEI, INAF-ORA (IRA)
(Istituto Nazionale di Astrofisica-Osservatorio di Radioastronomia)

## Slide 2
ON 1st August 2015 A MAJOR CHANGE OCCURRED IN ITALIAN RADIOASTRONOMY
IRA (Istituto di Radioastronomia) NO MORE EXISTS.
IT HAS BEEN MERGED WITH OAC (Osservatorio di Cagliari) TO BECOME
ORA (Radioastronomy Observatory)
AIM: UNIFY RESEARCH AND FACILITIES FOR ITALIAN RADIOASTRONOMY IN ONE SINGLE STRUCTURE.
SINCE 1st January 2016 DIRECTOR of ORA WILL BE STEVEN TINGAY (now at Murchison Widefield Array, Australia)
NOTICE: PLEASE, TAKE NOTE !

## Slide 3
NEW GENERATION 3mm-VLBI OBSERVATIONS CALLS FOR THREE ASPECTS:
INCREASED CAPABILITIES, i.e.
  STATE OF THE ART RECEIVERs,
  WIDEBAND
  LONGER INTEGRATION TIME at 3 mm
  MULTI-FREQUENCY (STATED AT 13, 7 and 3 mm BANDS)
  SIMULTANEITY or at least NEAR SIMULTANEITY WITH FAST BAND SWITCHING
DIMENSIONS OF THE RECEIVER AS THOSE ALREADY USED AT THE ANTENNA
ADDITION OF TELESCOPES
REQUIREMENTS 1d, 1e and 2 ARE PROFITABLY FULFILLED BY USING MULTIFEED TECHNIQUE
NEW DEMANDS FOR VLBI OBSERVATIONS

## Slide 4
IS A RECEIVING SYSTEM WITH 3 RECEIVER CHAINS (K, Q and W BAND) AT HAND TODAY? WITH WHICH PERFORMANCE?
COULD IT BE MADE SUCH THAT IT EASILY FITS IN ALMOST ANY (EVN) ANTENNA?
CHANCES TO OBSERVE NEAR SIMULTANEOUSLY OR SIMULTANEOUSLY WITH A
‘MINOR’ EFFORT OF R&D?
COULD THE TRI-FEED RECEIVER BE MADE AT AN ‘AFFORDABLE’ COST?
OVERVIEW OF THIS TALK

## Slide 5
570mm
7-feed
18-26 GHz
Cryostat
(includes cal injection)
700
EU-FP7- ’APRICOT’
630
19-feed
33-50 GHz
Cryostat
(includes 1° conv, cal injection and LO distribution)
850
400
Tri-feed
22/44/86 GHz
Cryostat
(includes 1° conv, cal injection and LO distribution)
650
K
Q
W
EU ??
TRI-FEED CRYOSTAT DIMENSIONS

## Slide 6
TRI-FEED TECHNOLOGY: EXAMPLES
67-116 GHz horn+omt
(INAF-OAA,Firenze,
Courtesy R. Nesti)
Talk at this Workshop
Option: reply as 7mm band (see Pisano’s talk) or other solutions
3mm band polarizer
3 mm BAND
33-50 GHz OMTs (INAF-OAA design)
33-50 GHz polarizers
33-50 GHz horn
(INAF-OAA design)
33-50 GHz cal injector
7 mm BAND
18-26 GHz horn to omt chain
(INAF-OAA design)
13 mm BAND
84-116GHz horn+omt
Courtesy G. Pisano, B. Maffei

## Slide 7
TRI-FEED ELECTRONICS: EXAMPLES
Cryo LNAs Power Supply Board
(Q and K band 2° conversion and W band 3° conversion)
(W band 2° conversion)
Front
Rear
Rear
Front
18-26 GHz to 6-8 GHz (K band 1° conversion)
W-CONV
75-110 GHz 1° conv. as K band technology
K-CONV
33-50 GHz to 1-18 GHz (Q band 1° conversion)
Q-CONV
LO Distributors (up to 18 GHz)

## Slide 8
ITALIAN TELESCOPES AVAILABILITY
Medicina: no active surface; max operating frequency = 26GHz
Noto: active surface equipped; overall surface accuracy today ≈ 400μm; possible ≈ 200 μm
K and Q bands available
Chart: SRT: Simulation at 22GHz, no active surface
| 10 | 15 | 20 | 30 | 40 | 45 | 50 | 60 | 70 | 75 | 80 | 90
 | 0.030458 | 0.067974 | 0.14321 | 0.39747 | 0.61282 | 0.65981 | 0.62099 | 0.39747 | 0.12424 | 0.046625 | 0.01221 | 0.00074867
SRT: active surface equipped; overall surface accuracy today = 300μm; future ≈ 180μm
-K band available,
-Q band under construction
-W band under implementation

## Slide 9
TRI-FEED ASSEMBLING AND PERFORMANCE ESTIMATION
Tri-feed
22/44/86 GHz
Cryostat
(includes 1° conv, cal injection and LO distribution)
600
480
400mm
650
Conversions, Control, LNA’s power supply, LOs distributor,
……
 | SRT |  |  | Noto (or Med upgraded) |  | 
 | 13mm | 7mm | 3.5mm | 13mm | 7mm | 3.5mm
Band (GHz) | 18-26 | 33-50 | 75-110 | 18-26 | 33-50 | 75-110
Tsys (K, zenith) | 700 | 60 | 1104 | 655 | 60 | 1104
G (K/Jy) | 0.661 | 0.52 | 0.193 | 0.156 | 0.146 | 0.16
SEFD (Jy) | 106 | 120 | 579 | 433 | 428 | 1100
Crosspol, D-term | ≈ 2% |  |  |  |  | 
NOTES 0: Measured (τ0=0.06) 1: Measured 2: with today surface accuracy = 300μm; 0.60K/Jy with surface accuracy = 180μm 3: with today surface accuracy = 300μm 0.44K/Jy with surface accuracy = 180μm 4: with τ0=0.2 5: Measured, new 18-26GHz receiver at Medicina (τ0=0.13) 6: with upgraded subreflector surface, rms ≤ 50μm |  |  |  |  |  | 

## Slide 10
K
Q
W
tilting subreflector
beams
primary mirror
Chart: Tri-feed: beam separation
| -2.0000000000000004 | -1.9000000000000006 | -1.8000000000000005 | -1.7000000000000004 | -1.6000000000000003 | -1.5000000000000002 | -1.4000000000000001 | -1.3 | -1.2 | -1.0999999999999999 | -0.99999999999999989 | -0.89999999999999991 | -0.79999999999999993 | -0.7 | -0.6 | -0.5 | -0.4 | -0.30000000000000004 | -0.2 | -0.1 | 0 | 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004
3.5mm | 0.017994 | 0.032 | 0.06706 | 0.063174 | 0.018087 | 0.044714 | 0.087427 | 0.079599 | 0.018159 | 0.066468 | 0.12367 | 0.11023 | 0.018211 | 0.11273 | 0.20753 | 0.1892 | 0.018242 | 0.28144 | 0.62473 | 0.8967 | 1 | 0.8967 | 0.62473 | 0.28144 | 0.018242 | 0.1892 | 0.20753 | 0.11273 | 0.018211 | 0.11023 | 0.12367 | 0.066468 | 0.018159 | 0.079599 | 0.087427 | 0.044714 | 0.018087 | 0.063174 | 0.06706 | 0.032 | 0.017994
13mm | 0.056123 | 0.024915 | 0.0097916 | 0.046569 | 0.083798 | 0.11972 | 0.1525 | 0.1803 | 0.20137 | 0.21406 | 0.21697 | 0.20895 | 0.1892 | 0.15727 | 0.11313 | 0.05717 | 0.0097961 | 0.086546 | 0.17148 | 0.26265 | 0.35785 | 0.45465 | 0.55049 | 0.64278 | 0.72895 | 0.80657 | 0.87342 | 0.92755 | 0.9674 | 0.99179 | 1 | 0.99179 | 0.9674 | 0.92755 | 0.87342 | 0.80657 | 0.72895 | 0.64278 | 0.55049 | 0.45465 | 0.35785 | 0.26265 | 0.17148 | 0.086546 | 0.0097961 | 0.05717 | 0.11313 | 0.15727 | 0.1892 | 0.20895 | 0.21697
7mm | 0.057443 | 0.09837 | 0.12367 | 0.1265 | 0.10357 | 0.056123 | 0.0097916 | 0.083798 | 0.1525 | 0.20137 | 0.21697 | 0.1892 | 0.11313 | 0.0097961 | 0.17148 | 0.35785 | 0.55049 | 0.72895 | 0.87342 | 0.9674 | 1 | 0.9674 | 0.87342 | 0.72895 | 0.55049 | 0.35785 | 0.17148 | 0.0097961 | 0.11313 | 0.1892 | 0.21697 | 0.20137 | 0.1525 | 0.083798 | 0.0097916 | 0.056123 | 0.10357 | 0.1265 | 0.12367 | 0.09837 | 0.057443
Tri-feed beams parameter |  | 
 | SRT | Med/Noto
 | (arcmin) | (arcmin)
FWHM 13 mm | 0.85 | 1.8
FWHM 7 mm | 0.48 | 0.9
FWHM 3.5 mm | 0.25 | 0.5
W-K Beam separation | 1.32 | 2
W-Q Beam separation | 0.72 | 1.1
W to Q bands horn distance | 31 mm | 
W to K bands horn distance | 58 mm | 
Tri-feed beams switching |  | 
 | SRT | Med/Noto
 | (s) | (s)
W to K switching time | 1 | 0.5
W to Q switching time |  | 
TRI-FEED NEAR SIMULTANEITY IN ITALY: READY

## Slide 11
R&D FOR SIMULTANEOUS TRI-FEED
THE ADDED-ON DEVICE DIMENSIONS MUST BE COMPATIBLE
WITH THE ROOM AVAILABLE BETWEEN TOP OF THE CRYOSTAT
AND THE VERTEX OF THE PRIMARY MIRROR AND ALL AROUND
THE TRI-FEED.
AN EXAMPLE at Medicina/Noto secondary focus….
Goretex cover of the
secondary focus cabin
5 GHz
7 GHz
Tri-feed
Tri-feed
Incoming radiation
….and SRT
Rotating drum
<600mm
Tri-feed
22/44/86 GHz
Cryostat (incl. Noise cal and 1° conversion)
ADDED-ON DEVICE
600
480
400
650
Conversions, Control, LNA’s power supply, LOs distributor,
……

## Slide 12
Frequency Selective Beam Tilter
(Talk at this workshop: G. Pisano)
d
D
Critical parameters: D, d, f, loss
75-110 GHz mesh lens with multiple grids
(Pisano et al., Applied Optics 2013)
f= 160mm
D= 54mm
d= 2.3mm
loss= 2.5%
Chart: Tri-beams aligned
| -2.0000000000000004 | -1.9000000000000006 | -1.8000000000000005 | -1.7000000000000004 | -1.6000000000000003 | -1.5000000000000002 | -1.4000000000000001 | -1.3 | -1.2 | -1.0999999999999999 | -0.99999999999999989 | -0.89999999999999991 | -0.79999999999999993 | -0.7 | -0.6 | -0.5 | -0.4 | -0.30000000000000004 | -0.25000000000000006 | -0.24000000000000005 | -0.23699999999999999 | -0.23000000000000004 | -0.22000000000000003 | -0.21000000000000002 | -0.2 | -0.1 | 0 | 0.1 | 0.2 | 0.21000000000000002 | 0.22000000000000003 | 0.23000000000000004 | 0.23699999999999999 | 0.24000000000000005 | 0.25000000000000006 | 0.26000000000000006 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004
3.5 mm | 0.017994 | 0.032 | 0.06706 | 0.063174 | 0.018087 | 0.044714 | 0.087427 | 0.079599 | 0.018159 | 0.066468 | 0.12367 | 0.11023 | 0.018211 | 0.11273 | 0.20753 | 0.1892 | 0.018242 | 0.28144 | 0.45465 | 0.4894 | 0.49978 | 0.5239 | 0.55804 | 0.59169 | 0.62473 | 0.8967 | 1 | 0.8967 | 0.62473 | 0.59169 | 0.55804 | 0.5239 | 0.49978 | 0.4894 | 0.45465 | 0.41978 | 0.28144 | 0.018242 | 0.1892 | 0.20753 | 0.11273 | 0.018211 | 0.11023 | 0.12367 | 0.066468 | 0.018159 | 0.079599 | 0.087427 | 0.044714 | 0.018087 | 0.063174 | 0.06706 | 0.032 | 0.017994
7mm | 0.057443 | 0.09837 | 0.12367 | 0.1265 | 0.10357 | 0.056123 | 0.0097916 | 0.083798 | 0.1525 | 0.20137 | 0.21697 | 0.1892 | 0.11313 | 0.0097961 | 0.17148 | 0.35785 | 0.47398 | 0.49325 | 0.49901 | 0.51244 | 0.53153 | 0.55049 | 0.72895 | 0.87342 | 0.9674 | 1 | 0.9674 | 0.87342 | 0.72895 | 0.55049 | 0.53153 | 0.51244 | 0.49901 | 0.49325 | 0.47398 | 0.35785 | 0.17148 | 0.0097961 | 0.11313 | 0.1892 | 0.21697 | 0.20137 | 0.1525 | 0.083798 | 0.0097916 | 0.056123 | 0.10357 | 0.1265 | 0.12367 | 0.09837 | 0.057443
13mm | 0.21697 | 0.20895 | 0.1892 | 0.15727 | 0.11313 | 0.05717 | 0.0097961 | 0.086546 | 0.17148 | 0.26265 | 0.35785 | 0.45465 | 0.48362 | 0.49325 | 0.50285 | 0.49901 | 0.51244 | 0.522 | 0.53153 | 0.54103 | 0.55049 | 0.64278 | 0.72895 | 0.80657 | 0.87342 | 0.92755 | 0.9674 | 0.99179 | 1 | 0.99179 | 0.9674 | 0.92755 | 0.87342 | 0.80657 | 0.72895 | 0.64278 | 0.55049 | 0.54103 | 0.53153 | 0.49901 | 0.4894 | 0.47977 | 0.47012 | 0.46045 | 0.45078 | 0.44109 | 0.45465 | 0.35785 | 0.26265 | 0.17148 | 0.086546 | 0.0097961 | 0.05717 | 0.11313 | 0.15727 | 0.1892 | 0.20895 | 0.21697
TRI-FEED SIMULTANEITY: A PROPOSAL for R&D
K
Q
W
FSBT
f
subreflector
primary mirror
beams

## Slide 13
 | Note: for each telescope | Cost of materials
Q.ty | Component | (k€)
1 | FSBT | 30
3 | Feeds | 7
3+3 | Polarizers+Omts | 32
3 | Noise Cal Injectors | 12
6 | Cryo LNAs | 90
3 | LNAs Power Supply Boards | 15
10 | Frequency converters (incl. LOs distributor) | 185
3 | NoiseCal system | 25
1 | Cryogenics | 110
 | Cables, connectors,..... | 35
 | Total | 540
COST ESTIMATION OF THE COMPLETE TRI-FEED
red: specific design for each telescope

## Slide 14
THANK YOU !