## Slide 1: Space-VLBI Multi-frequency Capabilities
A. G. Rudnitskiy, S. F. Likhachev, V. I. Kostenko
A. S. Andrianov, I. A. Girin
Astro Space Center of Lebedev Physical Institute
Data Processing Department
Large Magellanic Cloud as Seen by Herschel and Spitzer
Credit: ESA/NASA/JPL-Caltech/STScI
Multi-frequency Mm-wave Radio Telescopes & Other Software Controlled Operations
October 5 – 7, 2015, Florence, Italy

## Slide 2: Radioastron Mission
The largest in the world 10-m deployable space radio telescope.
Launched on 18th of July, 2011
- Daily Space-VLBI observations
- Support from more than 30 ground radio telescopes around the world
- Orbit around the Earth up to 300 000 km
- More than 4 years of successful operation
- Multi-frequency observations capability (18392 – 25112 MHz)
Studies on:
- AGN+QSO (imaging, surveys)
- Masers (imaging, surveys)
- Pulsars (ISM, scattering effects, etc.)
Frequency bands:
316 MHz, 1660 MHz, 4868 MHz, 22220 MHz

## Slide 3: Millimetron Mission
The first 10-m deployable and cooled space sub-mm and FIR telescope.
Mission has been approved and supported by Russian Space Agency
- FIR, sub-mm and mm range
- In orbit deployable and adjustable antenna
- Cosmology and astrophysics studies
- Mechanically cooled (<10K) with post-cryo life
- Orbit around L2 Lagrange point
- Lifetime: 10 years; at cryo >3 years
Dual operation modes:
S-VLBI for: 1 – 17 mm
Single dish for: 0.06 – 3 mm
Spacecraft in Phase-B
Science payload in Phase-A
Launch date : 2020++

## Slide 4: (u, v) - coverage examples
Radioastron - VLBA
Millimetron - EHT (snap-shot)

## Slide 5: What is Multi-frequency Imaging?
The main idea of Multi-frequency imaging (MFI) is to obtain detailed information about a radio source (intensity distribution) and its spectral parameters (e.g. spectral index) using the observations in a wide frequency range.
In 1998 a task was stated at ASC LPI to develop a receiver in frequency range from 18 to 25 GHz for “Radioastron” project in order to improve the (u, v)-coverage at least up to 30%.

## Slide 6: Multi-frequency Imaging
Multi-frequency imaging (MFI) consists of:
Multi-frequency synthesis (MFS): image synthesis and deconvolution procedures (CLEAN, etc.)
Multi-frequency analysis (MFA): estimation of the image parameters (spectral indexes, etc.)

## Slide 7: Advantages
MFI provides enhanced angular resolution and quality for any image due to improved (u, v)-coverage and, hence, better parameters of the dirty beam!
Improvement of (u, v)-coverage and increasing of dynamic range of the deconvolved image of the radio source.
Map synthesis for spectral index and its frequency dependence (including possibility of polarization parameter estimation as well as Faraday rotation measure and polarization imaging)
Differential astrometry and interstellar diffraction

## Slide 8: Multi-frequency Imaging Formalism
If brightness in a given point can be represented as
Then the spectral index can be represented as
and, hence,
Considering metrics as
A dirty map in a give point will be:

## Slide 9: Comparison with Other Algorithms
Comparing to previously developed MFS algorithms (Sault, Conway, et. al.), current MFI approach is capable of:
Estimation of spectral index and image at reference frequency is performed together at several frequencies from directly measured visibility function on an united (u, v)-plane (instead of separate analysis of maps synthesized at each frequency separately with poor (u, v)-coverage)
Usage of N-order vector relaxation method (N – number of frequency channels) instead of empiric Double Deconvolution scheme (double usage of scalar CLEAN procedure)

## Slide 10: Astro Space Locator Software
Software package developed at Astro Space Center.
- Operates under Microsoft Windows and Linux.
- Provides all necessary instrumentations for VLBI data post-correlation editing, analysis and imaging.
- Includes the improved MFS and MFA algorithms.
ASL Software package MFS and MFA algorithms provide an ability to estimate spectral index map for any intermediate frequency in a given observational range.

## Slide 11: Multi-Frequency Imaging (3C84)
Observations done with VLBA.
8GHz
15GHz

## Slide 12: Multi-Frequency Imaging (3C84)
Observations done with VLBA.
Jet spectra:
Core spectra:

## Slide 13: Multi-Frequency Imaging (M51, 3C75)
Observations done with VLA.

## Slide 14: Multi-frequency Imaging (M87)
Observations done with VLA.

## Slide 15: Multi-Frequency Imaging (3C279)
Observations done with KVN (Korean VLBI Network). Courtesy of Taehyun Jung.
22GHz
43GHz
86GHz
129GHz

## Slide 16: MFS with Radioastron
Simulations were done for Radioastron - VLBA
Radioastron-VLBA
Model - three delta functions:
Flux [Jy] Distance [as]
Delta func. 1 1 0
Delta func. 2 0.5 910-6
Delta func. 3 0.5 1.210-5

## Slide 17: MFS with Radioastron
No MFS
With MFS

## Slide 18: MFS with Radioastron
Radioastron capable of observing in MFS at K-band:
Sub-Band No | Sub-Band (MHZ) | SEFD SRT (kJy) | 5dS GBT-SRT (mJy) (*
F-4 | 18 392 | 26 | 700
F-3 | 19 352 | 28 | 740
F-2 | 20 312 | 31 | 775
F-1 | 21 272 | 34 | 815
F0 | 22 232 | 37 | 850
F1 | 23 192 | 41 | 890
F2 | 24 152 | 46 | 950
F3 | 25 112 | 51 | 1000
One polarization channel (RCP or LCP) operates at a fixed frequency, while the second polarization channel switches frequency in steps of 960 MHz starting at the lowest value of 18392 MHz, which corresponds to the 512 MHz IF input of the Formatter. The highest frequency is 25112 MHz.
*) Δ f = 36 MHz, Tau = 600 sec, SEFDGBT = 15 Jy

## Slide 19: MFS with Millimetron
Using ASL Software package were performed simulations for MFS observations of Sgr A* with simple model and several models provided by Jason Dexter (Dexter et. al., 2013).
Simple model
One of the models provided by Jason Dexter
MFS is very important for Millimetron to improve the (u,v)-coverage taking into account orbital, thermal and other possible constraints.

## Slide 20: MFS with Millimetron
Millimetron-Event Horizon Telescope Simulation

## Slide 21: MFS with Millimetron
Millimetron-Event Horizon Telescope Simulation
Model
Dirty map
Clean map
Series of short snapshots merged together (total 8 days), each snapshot can be 5 minutes – 1 hour

## Slide 22: Conclusions
New MFI algorithms were developed and implemented in the Astro Space Locator Software. They were tested on the various VLBI data sets, proving the efficiency of MFS.
MFS can essentially improve the UV coverage and increase the dynamic range of the output image.
MFS approach is critical issue that must be used in Space-VLBI missions, like Radioastron and Millimetron, to reduce possible mission constraints.

## Slide 23: Thank you for your attention!
Contacts:
Astro Space Center, Lebedev Physical Institute (ASC LPI) Russian Academy of Sciences
On behalf of Data Processing Department ASC LPI:
S. F. Likhachev
E-mail: slikhach@asc.rssi.ru
V. I. Kostenko
E-mail: vkostenko@asc.rssi.ru
A. G. Rudnitskiy
E-mail: almax1024@gmail.com, arud@asc.rssi.ru
Large Magellanic Cloud as Seen by Herschel and Spitzer
Credit: ESA/NASA/JPL-Caltech/STScI